This routine is a resident keyboard interrupt interceptor which displays
the status of the Capslock and Numlock keys.  If Capslock is on, a "C"
will be displayed in the upper right hand corner of the display.
Similarly, a "N" signifies the Numlock mode.

     The display is updated after each keystroke.  That is, if you
install KEYSTAT with capslock on, nothing will be displayed until
AFTER you strike a key (for more details, see below).

To use the program, type
     KEYSTAT ON
to install the program or
     KEYSTAT OFF
to cancel it.  To display the current state, type
     KEYSTAT
The command syntax is patterned after the DOS BREAK command.

This program requires DOS 2.0 or later.  If loaded on a pre-DOS 2.0 system,
an error message is displayed.

This routine is called each time a key is pressed.  It will remain resident
until the system is rebooted or cancelled via the OFF command.  Note, however,
that the memory allocated to the program when it is installed is NOT freed
when the routine is turned OFF.  The resident portion of the program takes
about 650 or so bytes of memory although the operable portion of the program
(that is, the code that is executed each time a key is pressed) is around
150 bytes; the available memory reported by CHKDSK, etc... is decreased when
KEYSTAT is loaded.  Turning KEYSTAT ON, then OFF, then ON again will load another
copy of the program into memory, decreasing the available memory even further.
This should not be a problem unless you do this twenty or thirty times.

KEYSTAT simply inserts itself "in series" behind the existing interrupt handler
and thus SHOULD be compatible with other keyboard utilities such as PROKEY,
etc... as long as they follow the IBM coding guidelines.  Other programs
may or may not be compatible with KEYSTAT.  I do not have any of these other
programs, so there is no way for me to test KEYSTAT with them.  Let me know
if you have problems using other programs with KEYSTAT.

This program is adapted from an aritcle in October '83 PC-World Magazine,
page 267.  The author of the original version, called KEYFLAGS, is Morton
Kaplon.  I found KEYFLAGS to be extremely userful and, as an excercise,
decided to write my own version.  In the process, I ended
up adding a few enhancements and changed the name to KEYSTAT.

Here is a summary of the differences between KEYFLAGS and KEYSTAT:
   1. All absolute references to BIOS in KEYFLAGS are replaced by
      interrupts in KEYSTATS.
   2. When KEYSTATS is loaded, it checks to see if it was already
      resident.  KEYFLAGS resets the vector every time, thus allowing
      nesting the code several levels deep.  This was unnecessary since
      the display need only be update once for every keystroke.  Additionally,
      it was undesireable since it would often hang the system.
   3. KEYFLAGS assumed that BIOS was servicing INT 9 and thus
      precluded using PROKEY, etc... with it.  KEYSTAT makes no such
      assumptions.  The previous keyboard service routine, be it BIOS, PROKEY,
      or whatever, is saved and that routine is re-installed when
      KEYSTAT is turned OFF.
   4. Because KEYSTAT uses the new DOS INT 35h, it requires DOS 2.0.
      There is no real reason why this could not be changed to get the
      current interrupt vector directly from memory so that any DOS version
      could be used, but it makes the code a little cleaner.  KEYFLAG can
      be used with any existing version of DOS but compatibility with
      future release is questionable.  KEYSTAT should be compatible with
      future releases of DOS.
   5. KEYFLAGS uses the "@" symbol to signify caps state and the "#" for
      numlock state.  I found these rather cryptic and changed them to
      "C" and "N", respectively in KEYSTAT.
   6. As mentioned earlier, I added command line parameters in KEYSTAT to
      allow for turning the routine OFF and to make it easy to use.
   7. A bug in KEYFLAGS has been fixed in KEYSTAT.  The bug occurs when
      the program is resetting the vector for INT 9.  Should an interrupt
      occur while the vector is being reset, the system will go off into
      computer "never-never land" the next time you press a key.  KEYSTAT
      disables interrupts while this critical section of code is executed.
      Admittedly, this is a rare bug in actual occurence, but it is still
      a bug.

You may make and distribute as many copies of this program as you wish.
Feel free to modify, mutilate, or adulterate this program.  If you come
up with an bug or improvement, please let me know by writing me at this
address:
        Tony A. Rhea
        1030 Ivy Lane
        Cary, NC  27511
If you do modify it, please give both myself and the original author
(Morton Kaplon) credit in the program.  This helps to preserve our egos
and increase our fame (but, unfortunately, NOT our fortunes).  Also, I
would appreciate a copy of the modified version, preferably on disk (I'll
be happy to return your diskette).

If you like this program ( or HATE it ), please let me know.  Drop me
a line at the address given above.

This program has been submitted for publication in PC-WORLD magazine.

I have experimented with an extension of this routine which also displays
the INSERT and SCROLL-LOCK states as well but found that it caused too much
overhead -- one could easily "outtype" the system.  Using DOS function 2
to automatically advance the cursor could eliminate the necessity of moving
the cursor thru INT 10h since the cursor is automatically advanced when
the character is displayed.  However, the current display attribute is
used so the status characters don't stand out very well.  Using DOS function
9 and printing all the status characters at once from a (constructed) string
would also work and would allow specifying an "attribute" to use (see the
discussion of "Extended Screen and Keyboard Control" in chapter 13 of the
DOS 2.0 manual).  However, that attribute will still be in effect after
the status characters are displayed.

The initialization code is overlaid by the next program DOS loads so that
only the ego statement, some variables, and the operable code remain resident.

The video positions are fixed (but can be changed in the equates below)
and thus will wipe out anything another program puts there.  It is best
not to put these at the bottom of the screen because the characters would
be scrolled up.  Putting them at the top of the screen solves this problem.

KEYSTAT waits until BIOS (or whoever) has serviced the keyboard interrupt
before it updates the display.  This is because it uses the KB_FLAG that
BIOS (or it's predecessor) must update.  If the user presses the Capslock key,
KEYSTAT lets the flag be updated first and then gets the flag to sense the
keyboard status.  If KEYSTAT had updated the display before letting the
original interrupt servicer update the flag, the display would not be correct
until the NEXT key is pressed.

Note that INT 25h CANNOT be used for setting a vector permanently.  When your
program terminates, DOS resets any vectors your program changes.  The only
way to make the change permanent is by a direct move into the vector table.

I have made heavy use of macros in KEYSTAT -- I find that it enhances the
readability greatly.  The code is not anything fancy nor is it particuarly
good, but it works.  This was my first big assembler program (by big I mean
anything over 10 lines long).  KEYSTAT is a pieced together from code fragments
from KEYFLAGS and other book and magazine articles.  Therefore, if you find
that I pushed CS/restored DS when I didn't really need to, it is certainly
because of my lack of understanding the deeper truths of assembler.  Please
feel free to improve upon KEYSTAT in any way you see fit.

Pseudocode:

  if not(DOS 2.0) then
     error message
     exit
  else
     { we have 2.0 - decode parm }
     get command line parameter
     convert to uppercase
     if (null parameter) then
        { display current status }
        if (already installed) then
           on message
        else
           off message
        endif already installed
     else
        { we got a parameter - see if it matches ON }
        if (ON) then
           if (already resident) then
              on message
              exit
           else
              make resident
              on message
              terminate, leaving operable code resident
           endif already resident
       else
           { command wasn't ON -- is it OFF? }
           if (OFF) then
              if not(already installed) then
                  off message
                  exit
              else
                 reset keyboard vector to original servicer
                 off message
                 exit
              endif not already installed
           else
              { we got a command that wasn't OFF or ON }
              error message
              exit
           endif off
        endif on
     endif null parameter
  endif not dos 2.0


  Revision history:
     rev 1.0  10/15/83                         { original release }
     rev 1.1  10/29/83                         { speed improvement }


Copyright (C) 1983  Tony Alan Rhea
This program may be copied and distributed for personal use
but not for profit provided this notice is included.  Author makes
no warranty, expressed or implied, as to the correct nature and
operation of this software.