Multi Spooler Ver. 2
                         for the IBM PC
                         by Rich Winkel
                          Columbia, Mo.

                   For free distribution only

                        Mspool2 Features

     Allows spooling up to 4 printers simultaneously.
     Supports both parallel and serial printers in any 
          combination.
     Has a user selectable buffer size up to 63K bytes.
     Sensitive to competing demands for CPU time.  Won't 
          slow down foreground jobs.
     Allows cancellation of an on-going print operation.
     Can be 'disabled' for use with programs which are 
          incompatible with it's operation.


Usage:    

To install the spooler, at the DOS prompt type:

          MSPOOL a b c
where:

a (= 1 - 4) represents the four possible printers on the PC.
            (1, 2 & 3 correspond to LPT1, LPT2 & LPT3)

b (= 1 - 9) represents the number of 7K chunks of memory to set 
            aside for the spooler buffer.

c (= 1 - 4) is an optional parameter used when you wish the
            output to be directed to a serial port.
            (1 and 2 correspond to COM1 and COM2)

     Once the spooler is installed, the user need not worry about 
it further; it will begin intercepting all print operations and 
buffering them.  However, the operation of the spooler can be 
modified after it has been installed, if the need arises.  After 
the spooler has been installed, if you type:

          MSPOOL a

     where 'a' is the same 'a' you used to install it, you are 
presented with three options: Purge, Disable or Enable.  These 
are as follows:

Purge:    Drops any characters remaining in the spooler buffer.  
          This has the effect of canceling any printing operation 
          currently taking place.

Disable:  A few programs for the PC operate in a way which 
          interferes with MSPOOL's ability to send characters to 
          the printer.  The result is that MSPOOL captures the 
          characters, but doesn't actually begin printing them 
          until it's buffer is full or you exit your program.  
          'Disabling' the spooler (prior to running your program) 
          keeps the number of characters in it's buffer from 
          growing.  That is, every time the spooler intercepts a 
          character, it prints a character.  If it's buffer is 
          empty, it's as if it wasn't there at all.  It simply 
          prints the character it gets when it gets it.  If there 
          are characters in the buffer at the time the offending 
          program is invoked, then when it gets a character to 
          print, it fetches the next character in line and prints 
          it, and puts the new character at the end of the queue.
          
Enable:   Re-enables spooling.

     Hitting any key other than P, D or E has no effect.

Notes:    

     To spool to a serial printer, first initialize the COM port 
with the MODE command: MODE COMc:baud,parity,databits,stopbits 
etc.  DO NOT use the P (continuous retry) option.  Then install 
MSPOOL: MSPOOL a b c.  This will route all output for LPTa 
through the spooler to the COMc port.  DO NOT use the MODE 
redirect command. (i.e. don't use MODE LPT#:=COMn)

     To spool to more than one printer, just run the spooler 
repeatedly, specifying each printer in turn.  

     When spooling to more than one printer, in certain 
circumstances (see tech hype below) the last spooler loaded will 
have priority, then the second to last.

     In order for the Purge, Disable, Enable routine to work, you 
should load the spooler(s) last among the 'resident' routine(s) 
which affect the operation of any printer.  For instance, if you 
use GRAPHICS.COM, you should run it before running MSPOOL.

     Once the spooler is installed, it's output cannot be re-
directed to another port, so programs written for this purpose 
(such as QSWAP) will not work.

     The ability to redirect to a COM port could be put to good
use when uploading a large file to another computer when no 
handshaking (XON/XOFF or XMODEM) protocol is required. 
(Especially if you are limited to 300 baud)

     More DOS Bugs!  Apparently, FORMAT & DISKCOPY will not work
properly if they do not reside low enough in memory, so if you have
trouble with either of these commands and you have a large spooler
buffer or a lot of resident routines installed, try rebooting
without the resident routines or reduce the spooler buffer size and
try again.  (This problem appears to be similar to the one which
arises if you have too much memory.)

Technical hype:

     This spooler intercepts 2 interrupts: Printer I/O (INT 17H), 
and Keyboard I/O (INT 16H).  At installation, it stores the old 
vectors for these interrupts internally and substitutes it's own 
addresses in the interrupt vector table.  
     Any call to print is checked as to whether it references the 
spooler's printer.  If not, it is passed on to the the old 
printer I/O handler. (could be another spooler, GRAPHICS.COM, the 
ROM routine etc.)  If it does reference the spooler's printer, 
the character is put in the spooler's buffer, and the buffer is 
checked to see if it's full.  If not, the spooler returns
to the calling program.  Otherwise, the spooler prints the
next character waiting in the buffer, then returns.  If the 
spooler has been 'disabled', it always prints the next character 
in the buffer, regardless of whether the buffer is full.
     Whenever a program makes a keyboard I/O call (INT 16H), the 
spooler checks whether it has a character to print in it's 
buffer.  If not, it passes control to the old keyboard I/O 
routine (could be another spooler, the ROM routine etc.).  
Otherwise, it makes one attempt to print a character.  It then 
checks to see if the keyboard call will require the keyboard I/O 
routine to wait for a character to be entered from the keyboard 
if no character is already in the keyboard buffer.  If not, it 
passes control to the old keyboard I/O handler.  Otherwise, it 
looks at the BUFFER_HEAD and BUFFER_TAIL words in the ROM BIOS 
data area to determine if there is a character in the keyboard 
buffer.  If there is, it passes control.  Otherwise, it begins 
looping, repeatedly attempting to print and checking the keyboard 
buffer until it either runs out of characters or a character is 
entered at the keyboard.  It is during this looping process that 
the most recently installed spooler will get the highest 
priority.  
     Whenever mspool is run, it checks where the printer I/O 
interrupt vector is pointing to determine whether it has already 
been installed.  If it doesn't find a copy of itself there, it 
assumes it is not installed and continues with installation.  If 
there is a copy of itself, it checks to see whether the copy is 
configured to intercept calls to the same printer as was 
specified in it's own parameter list (parm 1). If not, it gets 
the segment for the next printer I/O handler up the line from the 
copy and repeats the same procedure until it either lands in 
unfamiliar territory or finds a spooler configured for it's 
printer.  If it finds one with the proper configuration, it 
presents you with the 'Purge, Disable, Enable' option.  
Otherwise, it continues with installation.
     During installation, the spooler is patched in accordance 
with the parameters passed to it by DOS, to customize for 
parallel or serial printing, buffer size, LPT number and the 
addresses of the old interrupt routines gotten from the interrupt 
vector table.
     The legal ranges for the printer number and serial port number
are due to the fact that there is space for 4 ports in both the
printer and RS-232 tables.
rt number
are due to the fact that there is space for 4 ports in both the
printer and RS-232 tables.