This is file: FCONSOLE.DOC.

        It is readable on-line.  It is also printable  on  most  printers, if
        they are first set to print 66 lines per page (no perforation skip).




             FANSI-CONSOLE (tm) User Manual             _____________ ____             FANSI-CONSOLE (tm) User Manual
             Version 1.07 - March 21st, 1985             Version 1.07 - March 21st, 1985


             No Smoking Software (tm)             __ _______ ________ ____             No Smoking Software (tm)


             (C) Copyright 1984-85             (C) Copyright 1984-85
             Hersey Micro Consulting, Inc.             Hersey Micro Consulting, Inc.
             P.O. Box 8276             P.O. Box 8276
             Ann Arbor, Michigan USA 48107             Ann Arbor, Michigan USA 48107
             (313) 994-3259 Voice             (313) 994-3259 Voice
             (313) 994-3946 BBS (11PM-8AM ET)             (313) 994-3946 BBS (11PM-8AM ET)

             ISBN 0-933737-01-7             ISBN 0-933737-01-7





        FANSI-CONSOLE      NOT                                         FANSI-        _____________                                                  ______        FANSI-CONSOLE  is  NOT a free program.  Usage and copying  of  FANSI-
        CONSOLE        _______        CONSOLE and its abbreviated user  manual  are  subject  to  extremely
        friendly licensing terms found within this manual.

































        Dedicated in memory of Ralph Emerson Hersey, inventor, pioneer in the
        communications  industry,  and  proud  grandfather.  In his  day,  he
        solved some of the world's  problems.  We hope we may all do the same
        in ours.  We can still hear him say, "That's the system".



























































        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)






                             Table of Contents


        Chapter 1 Introduction                                          1

                       FANSI-CONSOLE                       _____________           1.1 What is FANSI-CONSOLE?                                   1
                         FANSI-CONSOLE                         _____________           1.2 What does FANSI-CONSOLE do?                              2

              1.2.1 Speeds up screen painting                           2
              1.2.2 Processes ANSI X3.64 escape sequences               3
              1.2.3 Emulates DEC VT100                                  4
              1.2.4 Allows much more typeahead                          5
              1.2.5 Allows more memory for key replacements             5
              1.2.6 Turns display off when not in use                   5
              1.2.7 Allows one finger pausing                           6
              1.2.8 Allows one finger typing                            6
              1.2.9 Allows keyboard generated breakpoints               6
              1.2.10 Eliminates screen flicker                          6
              1.2.11 Provides support for 50 line displays              7
              1.2.12 Extends the IBM-PC ROM BIOS                        7
              1.2.13 Other features                                     7

           1.3 What about multitasking windowing programs and
                       FANSI-CONSOLE                       _____________                       FANSI-CONSOLE?                                   8

        Chapter 2 Starting Quickly                                      10

                                           FANSI-CONSOLE                                           _____________           2.1 Do I have to read the whole FANSI-CONSOLE user
                       manual?                                          10

              2.1.1 NO!                                                 10

                                        FANSI-CONSOLE                                        _____________           2.2 How do I quickly install FANSI-CONSOLE?                  11

              2.2.1 Verify distribution diskette                        11
              2.2.2 Backup distribution diskette                        13
              2.2.3 Backup system disks                                 13
              2.2.4 Copy FCONSOLE.DEV to system disk                    13
              2.2.5 Add DEVICE=FCONSOLE.DEV to CONFIG.SYS               14
              2.2.6 Remove DEVICE=ANSI.SYS from CONFIG.SYS              14
              2.2.7 Restart MS(PC)-DOS                                  16
              2.2.8 Add BUFFERS=20 to CONFIG.SYS                        17
              2.2.9 Modify Prompt                                       18
              2.2.10 Provide memory for applications programs           20

                            FANSI-CONSOLE                            _____________           2.3 How do I use FANSI-CONSOLE?                              21

              2.3.1 Using the Ctrl-F key                                21
              2.3.2 Using the Ctrl-S key                                21

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


              2.3.3 Using the Ctrl-Num-Lock key                         22
              2.3.4 Using the Ctrl-C or Ctrl-Break keys                 22
              2.3.5 Using the Ctrl-Equals key                           22
              2.3.6 Using the Shift-PrtSc key                           23

                                  FANSI-CONSOLE                        __        _____________           2.4 How do I uninstall FANSI-CONSOLE?                        24

        Chapter 3 Detailed Installation                                 25

           3.1 So what is an MS(PC)-DOS device driver, anyway?          25
           3.2 What if my computer is ... different?                    27

        Chapter 4 Programming Background                                38

           4.1 Which screen access method is best?                      38

        Chapter 5 ANSI X3.64 escape sequences                           41

           5.1 Why use ANSI X3.64?                                      41
           5.2 What is an ANSI X3.64 escape sequence?                   42
           5.3 How can my program write the ANSI X3.64 escape
                       sequences?                                       44

              5.3.1 BASIC                                               45
              5.3.2 C                                                   46
              5.3.3 PASCAL                                              47
              5.3.4 Assembly Language                                   48

           5.4 What can the ANSI X3.64 escape sequences do?             51
           5.5 How do I find out the name of an ANSI X3.64 escape
                       sequence?                                        97

        Chapter 6 ROM BIOS Calls                                        102

           6.1 Do I have to change my ROM BIOS calls?                   102
           6.2 How do I make keyboard BIOS calls?                       104
           6.3 How do I make display BIOS calls?                        110

        Chapter 7 Advanced Features                                     118

                                          FANSI-CONSOLE                                          _____________           7.1 How do I assign strings to FANSI-CONSOLE keys?           118
           7.2 How do I induce breakpoints with the keyboard?           121

              7.2.1 Using the Alt-Ctrl-Ins key                          121

                            FANSI-CONSOLE                            _____________           7.3 How do I get FANSI-CONSOLE to emulate a VT100?           122

              7.3.1 Using the Alt-Ctrl-Num-Lock key                     122

                            FANSI-CONSOLE                            _____________           7.4 How do I get FANSI-CONSOLE to be more compatible?        125

              7.4.1 Using the Alt-Ctrl-Down key                         125


        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


                            FANSI-CONSOLE                            _____________           7.5 How do I get FANSI-CONSOLE to be faster?                 125

              7.5.1 Using the Alt-Ctrl-Up key                           125

           7.6 How do I get the console into local mode?                126

              7.6.1 Using the Alt-Ctrl-Scroll-Lock key                  126

           7.7 How do I access the original definition of a key?        127

              7.7.1 Using the Alt-Ctrl-Caps key                         127

           7.8 How do I get a Dvorak keyboard arrangement?              128

              7.8.1 Using the Alt-Ctrl-Tab key                          128

           7.9 How do I get back the normal keyboard arrangement?       128

              7.9.1 Using the Alt-Ctrl-Esc key                          128

           7.10 What do the extra distribution files do?                129

        Chapter 8 Compatibility and Limitations                         130

                                     FANSI-CONSOLE                                     _____________           8.1 What limitations does FANSI-CONSOLE have?                130
                                             FANSI-CONSOLE                                             _____________           8.2 Are there several versions of FANSI-CONSOLE?             131
                                                 FANSI-CONSOLE                                                 _____________           8.3 What programs are compatible with FANSI-CONSOLE?         132
                                                  FANSI-CONSOLE                                                  _____________           8.4 What computers are compatible with FANSI-CONSOLE?        135
                                                   FANSI-CONSOLE                                 __                _____________           8.5 What programs are incompatible with FANSI-CONSOLE?       136
                                                    FANSI-CONSOLE                                  __                _____________           8.6 What computers are incompatible with FANSI-CONSOLE?      138

        Chapter 9 Credits                                               141

           9.1 How did you do that?                                     141

        Chapter 10 Distribution and Licensing                           143

                         FANSI-CONSOLE                         _____________           10.1 You mean FANSI-CONSOLE isn't freeware?                  143
                                               FANSI-CONSOLE                                               _____________           10.2 How are you limiting my use of FANSI-CONSOLE?           145

              10.2.1 Limitations                                        145
              10.2.2 Rights                                             148

                                 FANSI-CONSOLE                                 _____________           10.3 How do I know if FANSI-CONSOLE is right for me?         149

              10.3.1 DISCLAIMER                                         149

                                                 FANSI-CONSOLE                                                 _____________           10.4 How do I get updated versions of FANSI-CONSOLE?         150
           10.5 What do we pay if we have more than one computer?       151
                                             FANSI-CONSOLE                                             _____________           10.6 Can I get a printed complete FANSI-CONSOLE user
                       manual?                                          152
                                  FANSI-CONSOLE                                  _____________           10.7 Can I publish the FANSI-CONSOLE complete user
                       manual?                                          154

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


                              FANSI-CONSOLE                              _____________           10.8 Can I buy the FANSI-CONSOLE program source?             154





















































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)                                       Introduction        _____________ ____        FANSI-CONSOLE (tm)                                       Introduction








                                      Chapter 1                                      Chapter 1

                                     Introduction                                     Introduction




                    FANSI-CONSOLE        __________________________        1.1 What is FANSI-CONSOLE?


                             FANSI-CONSOLE (tm)                             _____________ ____        Briefly, the program FANSI-CONSOLE (tm) is a fast ANSI X3.64 standard
        console driver for the IBM-PC, running under  MS(PC)-DOS.   The  name
        "FANSI"  comes  from  "fast  ANSI".  It is  pronounced  the  same  as
        "fancy".  The "CONSOLE"  is  what  we  call  the  screen and keyboard
        together.  "MS(PC)-DOS" is the name we use for Microsoft's MS-DOS, of
        which IBM-PC DOS is a variant.

                                                FANSI-CONSOLE                                                _____________        This chapter gives an overview of what  FANSI-CONSOLE can do for you,
        and explains why you'll want to use it.  The next chapter  tells  you
        how to get started, so that you can try it right away.




























        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 1        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 1








        FANSI-CONSOLE (tm)                                       Introduction        _____________ ____        FANSI-CONSOLE (tm)                                       Introduction






                      FANSI-CONSOLE        _______________________________        1.2 What does FANSI-CONSOLE do?


        FANSI-CONSOLE        _____________        FANSI-CONSOLE is both an MS(PC)-DOS console driver and a BIOS console
        driver.  These are two somewhat similar but still  different  things.
        Somewhat like an actor  playing  the  parts of both twins in a movie,
        FANSI-CONSOLE        _____________        FANSI-CONSOLE plays  the  part of the IBM-PC ROM BIOS console code as
                                                                FANSI-CONSOLE                                                                _____________        well as the part of the IBM-PC ANSI.SYS device driver.  FANSI-CONSOLE
        replaces the  screen  and  keyboard handling parts of both the IBM-PC
        ROM BIOS and the  MS(PC)-DOS  2.00  (and  later  versions)  operating
        system.   It  is  a  complete  replacement  for  the  IBM-PC  console
        software, but offers some significant improvements.

                                        FANSI-CONSOLE                                        _____________        Just like the operating system, FANSI-CONSOLE  is  always  in  memory
                                                                FANSI-CONSOLE                                                                _____________        once it is placed there during the  startup  process.   FANSI-CONSOLE
             ________  _____  ____  __  __________  ______        only requires  about  16KB  of  read/write  memory  for  itself.   In
        comparison, the IBM-PC ANSI.SYS device  driver  only  requires  about
                                                      FANSI-CONSOLE       not                                                      _____________       ___        1.6KB  of  read/write  memory  for  itself.   FANSI-CONSOLE does  not
        require any special hardware like a second  diskette drive or a fixed
        disk.  It performs just as well without them as with them.

        FANSI-CONSOLE        _____________        FANSI-CONSOLE works on  most  computers which are hardware equivalent
        to the IBM-PC.  These computers are sometimes called "compatibles" or
        "clones".   Please  note that because of the nature of  the  program,
        FANSI-CONSOLE        _____________      ___                                  ___        FANSI-CONSOLE does not  work  on  machines  which  are  not  hardware
        equivalent to the IBM-PC.  For compatibility details please refer  to
        the compatibility chapter contained within this manual.  We obviously
        hope to extend the compatibility list, as more people report how well
        it works on other machines.




        1.2.1 Speeds up screen painting        _____ ______ __ ______ ________        1.2.1 Speeds up screen painting

                                    FANSI-CONSOLE                                    _____________        The  most  basic feature of FANSI-CONSOLE is that it  speeds  up  the
        screen painting of  many  programs, including all MS(PC)-DOS internal
        commands.  "Screen painting" is what  we  call the process of filling
        the screen  with  information  by "writing" to it.  Any program which
        uses MS(PC)-DOS or  IBM-PC  ROM  BIOS  calls to access the PC screen,
                                                                   __ ____ __        instead of direct hardware manipulation, paints the screen as much as
                                                FANSI-CONSOLE        _____ _____ __ ____                     _____________        three times as fast as it does without  FANSI-CONSOLE.   Most  of the
        speed ups we've tested in our benchmarks range  between  1.3  and 2.0
        times  as  fast.  Other programs, those which write directly  to  the
        IBM-PC screen memory, are unaffected.  A program's screen painting is
                             FANSI-CONSOLE                             _____________        never slowed down by FANSI-CONSOLE.  This means much less waiting for
        menus and so on to be painted onto your screen.



        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 2        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 2








        FANSI-CONSOLE (tm)                                       Introduction        _____________ ____        FANSI-CONSOLE (tm)                                       Introduction


        Generally, programs that write to the screen slowly are the ones that
        are speeded  up.   Programs  written to run on any MS(PC)-DOS machine
        are speeded up.   Programs  that  are  quick to begin with are nearly
        always  the  programs that write directly to the screen  memory,  and
                                      FANSI-CONSOLE                      ___             _____________        therefore are not affected by FANSI-CONSOLE.  Also, any program  that
        causes hashing (snow) on an IBM-PC color graphics display adaptor are
                        FANSI-CONSOLE                        _____________        not affected by FANSI-CONSOLE, because it writes directly  to  screen
        memory.  For details about which programs are speeded up please refer
        to  the  compatibility  list  contained within the  chapter  entitled
        "Compatibility and Limitations".

        The amount of the speed up depends upon the type of  display  adaptor
        used, the screen mode, what type of screen  writing  calls  are used,
        whether scrolling is necessary, and what brand of  IBM-PC  equivalent
        machine you have.  Monochrome cards and  color  cards  which  do  not
        require screen memory accesses  to  be  delayed  until  a  horizontal
        retrace are generally  speeded  up  more  than  the  standard  IBM-PC
        graphics card.  The  alphanumeric  screen modes generally are speeded
        up more than the graphics screen  modes.   DOS  calls  are  generally
        speeded  up  more than BIOS calls.  Programs that require  no  screen
        scrolling  are  speeded  up  more  than  those  requiring  scrolling.
        Lastly,  some  IBM-PC  equivalent  computer  BIOSes  are slower  than
        others, and these are speeded up more than the fast ones.   The  best
        part is  that  the screen modes used the most, the alphanumeric modes
        with no scrolling, are speeded up the most.




        1.2.2 Processes ANSI X3.64 escape sequences        _____ _________ ____ _____ ______ _________        1.2.2 Processes ANSI X3.64 escape sequences

                                           FANSI-CONSOLE                                           _____________        Another important  feature is that FANSI-CONSOLE processes ANSI X3.64
        standard escape  sequences  like  the  IBM-PC  DOS  2.00  (and  later
                                           FANSI-CONSOLE                                           _____________ ______ _ ____ ______        versions) ANSI.SYS device driver.  FANSI-CONSOLE allows a much larger
        ______ __ ___  ________        subset of the  standard  to  be  used than the IBM-PC ANSI.SYS device
        driver does.  All escape sequences work in the  graphics screen modes
        as well as in the alphanumeric screen modes.  This means programs can
        do more versatile things with the screen in  a  simpler  and computer
        independent way.  This is directly  important  to  you  because  such
        programs can have their screen output sent to remote terminals, or be
        redirected to data  files.   Indirectly,  it  is  important  to  you,
        because it may have the effect of reducing  program development costs
        by making it easier to write things to the screen and by allowing the
        same  program  to  run  without change on  many  different  types  of
        computers.  Presumably,  the program developers will pass the savings
        on to you.  For more details, see the  chapter  entitled  "ANSI X3.64
        escape sequences".  Please note that  the  chapter  describing  these
                                         abbreviated                                         ___________        escape sequences  is  not in the abbreviated user manual found on the
        diskette, but  is  contained  in the complete printed user manual.  A
        few files are included on the diskette which give demos, though.




        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 3        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 3








        FANSI-CONSOLE (tm)                                       Introduction        _____________ ____        FANSI-CONSOLE (tm)                                       Introduction


        Using these escape  sequences  it  is  possible  to  limit the screen
        output of some programs to a  portion of the screen called a "window"
        or  a  "scrolling  region".   These  windows  can be scrolled in  any
        direction or otherwise modified without affecting text on the rest of
        the screen.   A  program  which knows about scrolling regions may use
        more than one scrolling  region  to  effectively  divide  the  screen
        display.  For more  details,  see  the  description  of  the ANSI SSR
        command  in  the  chapter  entitled  "ANSI  X3.64 escape  sequences".
        Please note that the chapter describing these escape sequences is not
                 abbreviated                 ___________        in  the  abbreviated user  manual  found  on  the  diskette,  but  is
        contained in the  complete  printed  user  manual.   A  few files are
        included on the diskette which give demos, though.




        1.2.3 Emulates DEC VT100        _____ ________ ___ _____        1.2.3 Emulates DEC VT100

        FANSI-CONSOLE        _____________        FANSI-CONSOLE can make the numeric keypad and function keys emulate a
        DEC VT100 auxiliary keypad.  With the processing of ANSI X3.64 escape
        sequences, this can make the IBM-PC  console look like a DEC VT100 to
        any application program.  This is useful because  there  are  already
        many  good  programs written for machines that use the  VT100  for  a
        console.  The console  handling  of  such  programs do not have to be
        rewritten  to  allow them to run on an IBM-PC.  It also means that  a
        simple terminal emulation (communications)  programs which use MS-DOS
                                   MODEM86 (tm)                                   _______ ____        console calls, such as our MODEM86 (tm) program, turns your IBM-PC or
        equivalent into an ANSI X3.64 standard terminal.  For  more  details,
        see the subsection entitled "Using the Alt-Ctrl-Num-Lock key" in  the
        chapter entitled "Advanced Features".

        FANSI-CONSOLE        _____________        FANSI-CONSOLE  can  also  emulate  a DEC VT52/Heath  H19/Zenith  Z100
        console as part  of  its  VT100  emulation.   For  more details about
        getting into this mode, see the subsection describing the ANSI DEC-SM
        command in the chapter entitled "ANSI X3.64 escape sequences".



















        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 4        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 4








        FANSI-CONSOLE (tm)                                       Introduction        _____________ ____        FANSI-CONSOLE (tm)                                       Introduction





        1.2.4 Allows much more typeahead        _____ ______ ____ ____ _________        1.2.4 Allows much more typeahead

        FANSI-CONSOLE        _____________        FANSI-CONSOLE has a much larger typeahead buffer  than  the  standard
        IBM-PC  typeahead  buffer.   Typeahead  is what your  keystrokes  are
        called when the currently running program is  not reading them at the
        moment.  Sometimes the program  is  busy  with  a  previous  command.
                                                                       FANSI-                                                                       ______        Other times the program just doesn't require keyboard input.   FANSI-
        CONSOLE        _______        CONSOLE  allows  127 characters of typeahead.   The  standard  IBM-PC
        typeahead buffer allows only 15 characters.  This means  you are much
        less likely to get that horrible beep  that means your keystrokes are
        being ignored because the currently running program is busy.  Because
        the  convenience  of  so  much  typeahead  also  brings  problems  of
                                                           FANSI-CONSOLE                                                           _____________        discovering that  you mistyped something early on, FANSI-CONSOLE also
                         _____  ___  _________  ______        allows  you  to  flush  the  typeahead  buffer with a Ctrl-F  without
        stopping what is currently running.   Also  Ctrl-C,  Ctrl-Break,  and
        Ctrl-S, all flush the typeahead buffer before  their  normal  action.
        This means you won't be ignored when you type these keys just because
        you happened  to  have  typed ahead something else earlier.  For more
                                                                FANSI-CONSOLE                                                                _____________        details,  see  the section entitled "How do I use  the  FANSI-CONSOLE
        keyboard?".




        1.2.5 Allows more memory for key replacements        _____ ______ ____ ______ ___ ___ ____________        1.2.5 Allows more memory for key replacements

        More memory  is  allowed  for  keyboard  key  replacements  than  the
                                                  FANSI-CONSOLE                                                  _____________        standard IBM-PC  ANSI.SYS device driver.  FANSI-CONSOLE allows you to
        specify how much memory is  used  for keyboard key replacements.  For
        more details, see the chapter entitled "Detailed Installation".




        1.2.6 Turns display off when not in use        _____ _____ _______ ___ ____ ___ __ ___        1.2.6 Turns display off when not in use

        FANSI-CONSOLE        _____________        FANSI-CONSOLE  can  be  configured  to  automatically  turn off  your
        console screen display when not in use for  a  specified  time.  This
        helps prevent you from permanently burning a particular display  onto
        your screen by leaving it on  the display too long.  Please note that
        to avoid surprising people, this is not the default action.  For more
        details, see the chapter entitled "Detailed Installation".









        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 5        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 5








        FANSI-CONSOLE (tm)                                       Introduction        _____________ ____        FANSI-CONSOLE (tm)                                       Introduction





        1.2.7 Allows one finger pausing        _____ ______ ___ ______ _______        1.2.7 Allows one finger pausing

        FANSI-CONSOLE        _____________ ______ ___ __ ___  __  ___ ___________ ___ ___ ________        FANSI-CONSOLE allows you to set  up  the Scroll-Lock key for optional
        ___  ______  _______        one  finger  pausing.  The Scroll-Lock key may be set up to act as  a
        scroll lock toggle, somewhat similar to the Ctrl-Num-Lock combination
        you are already familiar with.   However,  it allows you to typeahead
        before turning off the scroll lock.  With both  the Ctrl-Num-Lock and
                             FANSI-CONSOLE                             _____________        Scroll-Lock pausing, FANSI-CONSOLE prevents the duplicate lines which
        may appear  when  using  the  standard  IBM-PC  software.   For  more
        details, see the chapter entitled "Detailed Installation".




        1.2.8 Allows one finger typing        _____ ______ ___ ______ ______        1.2.8 Allows one finger typing

        FANSI-CONSOLE        _____________ ______ ___ __ ___ __  ___  ________  ___  ________  ___        FANSI-CONSOLE allows you to set up  the  keyboard  for  optional  one
        ______ ______        finger typing.  For more details, see the chapter entitled  "Detailed
        Installation".




        1.2.9 Allows keyboard generated breakpoints        _____ ______ ________ _________ ___________        1.2.9 Allows keyboard generated breakpoints

        FANSI-CONSOLE        _____________        FANSI-CONSOLE has Alt-Ctrl-Ins set up to generate the equivalent of a
        breakpoint.   This  comes  in  handy  when  debugging  programs  with
        infinite loops.  For more details, see the subsection entitled "Using
        the Alt-Ctrl-Ins key" in the chapter entitled "Advanced Features".




        1.2.10 Eliminates screen flicker        ______ __________ ______ _______        1.2.10 Eliminates screen flicker

        A feature that owners of IBM-PC color graphics  card equivalents like
                                                   FANSI-CONSOLE                                                   _____________        Tecmar's Graphics Master will love is that FANSI-CONSOLE  can be used
             _________   ______   _______   _______        to   eliminate   screen   flicker   (blink)   as   it  is   scrolled.
        Unfortunately, this is  not  so  on  the  IBM-PC  color graphics card
                                                                      __        because of  a  hardware  design deficiency (well, that's what we call
        it).   For  more  details,   see   the   chapter  entitled  "Detailed
        Installation".









        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 6        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 6








        FANSI-CONSOLE (tm)                                       Introduction        _____________ ____        FANSI-CONSOLE (tm)                                       Introduction





        1.2.11 Provides support for 50 line displays        ______ ________ _______ ___ __ ____ ________        1.2.11 Provides support for 50 line displays

        For display adaptors with enough memory  and  displays  with  a  long
        persistence phosphor, there is support for several 50 line interlaced
        display modes.  For more details, see the subsection  describing  the
        IBM-SM  command  in  the  chapter   entitled   "ANSI   X3.64   Escape
                                                             abbreviated                                                             ___________        Sequences".  Please note this chapter is not in  the abbreviated user
        manual  found  on  the  diskette,  but  is contained in the  complete
        printed user manual.




        1.2.12 Extends the IBM-PC ROM BIOS        ______ _______ ___ ______ ___ ____        1.2.12 Extends the IBM-PC ROM BIOS

                                                                       FANSI-                                                                       ______        Several additional capabilities have been added to the part of FANSI-
        CONSOLE        _______        CONSOLE which replaces  the  ROM  BIOS.   For  more  details, see the
        chapter entitled "ROM BIOS calls".   Please  note this chapter is not
                 abbreviated                 ___________        in  the  abbreviated user  manual  found  on  the  diskette,  but  is
        contained in the complete printed user manual.




        1.2.13 Other features        ______ _____ ________        1.2.13 Other features

        FANSI-CONSOLE        _____________        FANSI-CONSOLE will have  other  features which will become documented
        as they become ready for use.























        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 7        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 7








        FANSI-CONSOLE (tm)                                       Introduction        _____________ ____        FANSI-CONSOLE (tm)                                       Introduction






                                                           FANSI-CONSOLE        _________________________________________________________________        1.3 What about multitasking windowing programs and FANSI-CONSOLE?


                                                FANSI-CONSOLE                                                _____________        You may wonder whether you  should  use FANSI-CONSOLE instead of some
        of the new multitasking windowing programs  such  as  IBM's  TopView,
                                                                       FANSI-                                                                       ______        Quarterdeck's DESQ, or Microsoft's Windows, or whether to use  FANSI-
        CONSOLE                                 FANSI-CONSOLE        _______                                 _____________        CONSOLE with  one  of  these programs.  FANSI-CONSOLE is not meant to
        compete  directly  with  these  programs.  Such programs  are  called
        "multitasking" because they allow  several  programs  to  be  in  the
        middle  of  doing  their  respective "tasks" at  the  same  time.   A
        multitasking windowing program manages the screen for such tasks, and
        allows you to switch  between  tasks.   We want to make it clear that
        FANSI-CONSOLE                                  FANSI-CONSOLE        _____________                                  _____________        FANSI-CONSOLE  does  not handle multitasking.  FANSI-CONSOLE  may  be
                                                            FANSI-CONSOLE                                                            _____________        used with most  multitasking  windowing  programs.  FANSI-CONSOLE may
        not affect them  or  the  programs  running under them, since most of
        these multitasking windowing programs  write  directly  to the screen
        hardware.  There will  be  times,  though,  when you will want to run
        without the multitasking windowing program, to  do  things  like  run
        batch files or programs  with  command  line  parameters.   At  these
               FANSI-CONSOLE               _____________        times, FANSI-CONSOLE will be there to speed up screen access.

                        FANSI-CONSOLE                        _____________        We believe that FANSI-CONSOLE is generally a more helpful product for
        the budget  minded  customer  than  multitasking  windowing programs.
        FANSI-CONSOLE        _____________        FANSI-CONSOLE offers much  less  in  the  way  of  features than most
                                               FANSI-CONSOLE                                               _____________        multitasking  windowing  programs, but FANSI-CONSOLE uses  much  less
        read/write memory and no secondary memory like additional disks,  and
        costs  less than most multitasking windowing programs.   Multitasking
        windowing programs usually need much more than  256K and a fixed disk
        for quick execution or sometimes  any  execution!  All this memory is
        generally used to keep several programs  in memory at once as well as
        copies of their screen displays.  Requiring that much memory or fixed
        disks  means  that those of you who cannot afford to lay out so  much
        money per system are unable to use multitasking windowing programs.

        Even if you  can  afford  a  multitasking  windowing  program and its
        required extra hardware, you may find  that you don't like it as much
           FANSI-CONSOLE   FANSI-CONSOLE           _____________   _____________        as FANSI-CONSOLE.  FANSI-CONSOLE speeds up  the  screen  painting  of
        many programs  to  make them quick enough for your tastes.  When your
        favorite  application  program still takes awhile  to  do  something,
        FANSI-CONSOLE        _____________        FANSI-CONSOLE  allows  you  to  keep  typing  by  having  a  generous
        typeahead buffer.  Most multitasking windowing products do nothing to
        speed up the screen painting of  other  programs.   They  also  don't
        allow you to typeahead much.  In  fact,  many  actually  slow  things
        down, even though they claim  to  be "user-friendly".  However, it is
        generally  recognized  that  being  speedy  is  one   of   the   most
        user-friendly qualities of a product.

                               FANSI-CONSOLE                               _____________        Another reason to like FANSI-CONSOLE is that  once you install it, it
             ___        does not require separate installation  of  the programs you run with

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 8        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 8








        FANSI-CONSOLE (tm)                                       Introduction        _____________ ____        FANSI-CONSOLE (tm)                                       Introduction


        FANSI-CONSOLE        _____________        FANSI-CONSOLE.   Most  multitasking  windowing  programs  require   a
        sometimes laborious  installation process for each program you intend
        to run with the multitasking windowing program.



















































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 9        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                 9








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly








                                      Chapter 2                                      Chapter 2

                                   Starting Quickly                                   Starting Quickly




                                        FANSI-CONSOLE        __________________________________________________________        2.1 Do I have to read the whole FANSI-CONSOLE user manual?


        2.1.1 NO!

               ___        You do not have to read this whole manual from cover to cover to take
                     FANSI-CONSOLE                     _____________        advantage of FANSI-CONSOLE.  You only have to know  what  is  in this
                                             ______        chapter to get started.  If you want really  brief instructions, just
        ____        read the description of this chapter in the  table  of  contents!  We
        know how much you hate to have to read the manual before trying out a
        program.  Unfortunately, this program can't be menu driven because of
        its nature.

        We have provided an extensive index  at the end of this manual.  It's
        there to help you if you have  problems  finding  what  you  want  to
        know.  Please use it, especially if you don't  read  the  manual from
        cover to cover.  For example,  solutions  to many common problems can
        be found by looking  up  the  keyword "problem" in the index.  If you
        can't  find  something where you looked first in the  index,  let  us
        know!  We think the index should be  comprehensive.   That  minimizes
        the  number  of  calls  we  get asking about things which  are  fully
        explained in the manual but aren't found.

        If what you want to know is only found  in  the complete printed user
        manual  and  not the abbreviated user manual found on  the  diskette,
        then it's probably time you paid for a complete user manual.  You can
        tell this is the case when you  find  yourself  looking  for  a  page
        number referred to in  the  index  or table of contents that isn't in
        your abbreviated  user  manual.   The index and the table of contents
        are complete, but your abbreviated user manual found  on the diskette
           ___        is not!

                                                       FANSI-CONSOLE                                                       _____________        Lastly, even though it  is  possible  to  use  FANSI-CONSOLE  without
        reading the chapter on its distribution, please read it, too.  It has
        details which are important to us about what we expect in return from
                                       FANSI-CONSOLE                                       _____________        you for your being able to use FANSI-CONSOLE.





        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                10        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                10








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly






                                     FANSI-CONSOLE        ___________________________________________        2.2 How do I quickly install FANSI-CONSOLE?


                                          FANSI-CONSOLE                                          _____________        If you  are  in  a  hurry  to try FANSI-CONSOLE, the following is the
                                                                FANSI-CONSOLE                                                                _____________        simplest possible setup  procedure.   Bear in mind that FANSI-CONSOLE
                                    ___        has some features which can not be taken advantage of in  this  case.
        Further reading will allow you to take advantage of those features at
        a later time.




        2.2.1 Verify distribution diskette        _____ ______ ____________ ________        2.2.1 Verify distribution diskette

        The first step is to verify that  the  following  files  are  on  the
        distribution diskette:

        ANSI40.TXT        ANSI40.TXT       Test data for 40 column screen displays.  Chock full
                         of examples of  ANSI  X3.64  escape sequences.  TYPE
                         this file for a demo!

        ANSI80.TXT        ANSI80.TXT       Test data for 80 column screen displays.  Chock full
                         of examples of  ANSI  X3.64  escape sequences.  TYPE
                         this file for a demo!

        DIZZY.C        DIZZY.C          Source  for  C  program   which  generated  part  of
                         ANSI80.TXT.

        DOSEDIT.PCH        DOSEDIT.PCH      Patch file for DOSEDIT  program version of 05/09/84.
                         Read comments in this file for instructions.

        DOSEDIT2.PCH        DOSEDIT2.PCH     Patch  file for DOSEDIT2 program.  Read comments  in
                         this file for instructions.

        DVORAK.TXT        DVORAK.TXT       Test data  to set up a quasi-Dvorak keyboard layout.
                         Unless you know what a Dvorak keyboard layout is, we
                                                    NOT                                                    ___                         strongly suggest  that you NOT TYPE this file.  This
                         is not a real Dvorak layout, but only  an example of
                         key redefinition.

        FCONSOLE.DEV     FANSI-CONSOLE                         _____________        FCONSOLE.DEV     FANSI-CONSOLE itself.

        FCONSOLE.DOC     FANSI-CONSOLE abbreviated                         _____________ ___________        FCONSOLE.DOC     FANSI-CONSOLE abbreviated  user  manual.   This file
                         may include information about  the latest version of
                         FANSI-CONSOLE                         _____________                         FANSI-CONSOLE which is  not  yet in the printed user
                         manual.  PRINT or TYPE this file.  You are reading a
                         copy of it now!



        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                11        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                11








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly


        FCONSOLE.HST        FCONSOLE.HST     Revision history information.  This file may include
                                                                       FANSI-                                                                       ______                         information  about  the  latest  version  of  FANSI-
                         CONSOLE                         _______                         CONSOLE  which  is  not  yet  in  the  printed  user
                         manual.  PRINT or TYPE this file.

        SK.PCH        SK.PCH           Patch for Sidekick to keep it from  waking  up  when
                         Alt-Ctrl  is  pressed.   Use  Left-Shift-Right-Shift
                         instead.  See the  comments  in the file for details
                         on usage.

        SPIT.EXE        SPIT.EXE         Test program for slowly trying test data.  Use it to
                         display a file  on  the console, like the MS(PC)-DOS
                         TYPE command.  It waits, with no prompts, for you to
                         press a key between every line displayed.

        If the listed files are not all  there,  ask  whomever  you  got  the
        program from to provide the missing files.  They are supposed to give
        you all the files listed here.   There  may  be  additional  optional
        files on the diskette which not listed here.   Please  note  that the
                                                      abbreviated                                                      ___________        user manual which appears on this diskette is abbreviated.

        Chapters describing advanced features in  detail  have  been  omitted
                  abbreviated                  ___________        from the  abbreviated  user  manual on the diskette.  See the chapter
        entitled Distribution and Licensing.






























        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                12        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                12








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly





        2.2.2 Backup distribution diskette        _____ ______ ____________ ________        2.2.2 Backup distribution diskette

        The  second step is to  make  a  backup  copy  of  your  distribution
        diskette using the  DOS  DISKCOPY  command,  as  outlined  in the DOS
        manual.  Start out by making  sure  that the distribution diskette is
        write protected, so that you don't accidently destroy what's on it by
                __                       ____        copying to it instead of copying from it.  After all, the reason that
        you should make the backup  copy in the first place is so that you'll
        have extra copies in case one copy gets accidently destroyed.




        2.2.3 Backup system disks        _____ ______ ______ _____        2.2.3 Backup system disks

        The third step is to make backup copies of your MS(PC)-DOS  2.00  (or
        later versions) system diskettes using the DOS DISKCOPY  command,  as
        outlined in the DOS manual.  A system  disk  is  any  disk  with  the
                                                                          ___        MS(PC)-DOS operating system on it.  Many MS(PC)-DOS diskettes are NOT
        system disks.  The best way to tell if a diskette is a system disk is
        to put the diskette into drive A:  and restart MS(PC)-DOS by pressing
        Alt-Ctrl-Del.   If  MS(PC)-DOS  starts   without   further   changing
        diskettes, then the diskette is a system disk.  If you have  a  fixed
        disk and you can start MS(PC)-DOS  with  an  Alt-Ctrl-Del  without  a
        diskette in drive A:, then your fixed disk is  also  a  system  disk.
        However, it will not be necessary to make a backup copy of your fixed
                         FANSI-CONSOLE                         _____________        disk just to try FANSI-CONSOLE.

        If  your  DOS  version  is less than 2.00, then run out and  buy  the
                             FANSI-CONSOLE                             _____________        latest version now!  FANSI-CONSOLE  requires  at  least version 2.00.
        Many other programs soon will as well.  Don't get lost in the past.




        2.2.4 Copy FCONSOLE.DEV to system disk        _____ ____ ____________ __ ______ ____        2.2.4 Copy FCONSOLE.DEV to system disk

        The  fourth  step  is  to   copy   the  file  FCONSOLE.DEV  from  our
        distribution diskette to your MS(PC)-DOS 2.00 (or later) system disks
        using the DOS COPY command.  Do this to all your system disks, if you
        have  more  than one.  However, we suggest that you do them one at  a
        time.  Test each one for a few days, or a time period comfortable for
        you, before installing it on other system disks.  If you have a fixed
        disk, we  suggest  you try this on a diskette first before installing
        FANSI-CONSOLE        _____________        FANSI-CONSOLE on the fixed disk.  All this caution is merely to allow
                                          FANSI-CONSOLE                                          _____________        you to start your system without  FANSI-CONSOLE  if  there  are  some
        problems with it on your system.




        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                13        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                13








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly





        2.2.5 Add DEVICE=FCONSOLE.DEV to CONFIG.SYS        _____ ___ ___________________ __ __________        2.2.5 Add DEVICE=FCONSOLE.DEV to CONFIG.SYS

        The fifth step is to add the line:

             DEVICE=FCONSOLE.DEV             DEVICE=FCONSOLE.DEV

        to the beginning of the CONFIG.SYS file on your system disk,  in  the
        root directory.  If there is a CONFIG.SYS  file in the root directory
        on your system disk when  you  start MS(PC)-DOS, MS(PC)-DOS will read
        it  for  special instructions.  Here it is a special  instruction  to
                FANSI-CONSOLE                _____________        install FANSI-CONSOLE.  You must create the CONFIG.SYS file if  there
        is not already one  in  the  root directory on the system disk.  Your
        favorite editor may be used to do this.  It  is  important  that  the
        line be at the start  of the CONFIG.SYS file instead of the middle or
                                                    FANSI-CONSOLE                                                    _____________        the end.  This is mostly because the sooner FANSI-CONSOLE gets loaded
        and its  name  banner  is displayed, the sooner your larger typeahead
                                                                FANSI-CONSOLE                                                                _____________        buffer is ready to be used.  It  is also important that FANSI-CONSOLE
        be loaded  before  any  other device drivers that require keyboard or
        screen  handling,  such  as  mouse  device  drivers.  Otherwise,  the
        position of this line does not matter.

        It is important that the  "DEVICE=FCONSOLE.DEV"  line is ended with a
        carriage return, and not just with the end  of  the  CONFIG.SYS file.
                                                                  _______        There is a bug in MS(PC)-DOS 2.0 which causes such a line without the
        carriage return to yield the following strange looking message:

             Bad or missing FCONSOLE.DEVLE.DEV             Bad or missing FCONSOLE.DEVLE.DEV

        The repeated part of the name is really in the message.  This bug was
        fixed in MS(PC)-DOS 3.0.




        2.2.6 Remove DEVICE=ANSI.SYS from CONFIG.SYS        _____ ______ _______________ ____ __________        2.2.6 Remove DEVICE=ANSI.SYS from CONFIG.SYS

        The sixth step is to delete any lines like:

             DEVICE=ANSI.SYS             DEVICE=ANSI.SYS

        from the CONFIG.SYS file.  If you have a reference to another console
        driver, such as the IBM-PC ANSI.SYS device driver,  in the CONFIG.SYS
                                                           FANSI-CONSOLE                                                           _____________        file then  you  should remove it.  This is because FANSI-CONSOLE is a
        direct replacement for ANSI.SYS as well as the part of the IBM-PC ROM
        BIOS that deals  with  the  console.   They both have the name "CON:"
        when referred to later with other DOS commands.   They cannot coexist
                                                                       FANSI-                                                                       ______        and there is no point in trying to make them coexist  because  FANSI-
        CONSOLE        _______        CONSOLE has all the function of the ANSI.SYS device driver.



        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                14        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                14








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly


        Please note that it is only console drivers that  do  not  work  with
        FANSI-CONSOLE        _____________        FANSI-CONSOLE.  Device drivers for devices  other  than  the  console
                                      FANSI-CONSOLE                                      _____________        (CON:)  may   be  used  with  FANSI-CONSOLE.   Such  drivers  include
                                                                       FANSI-                                                                       ______        read/write memory-based diskette  emulators  (ram-disk)  like  FANSI-
        RAMDISK  (tm)        _______  ____        RAMDISK  (tm)  and mouse device drivers.  So most lines  which  start
        with:

             DEVICE=             DEVICE=

        do not need to be deleted from CONFIG.SYS.

        If you happen to load both drivers, the one  which  is loaded last is
        the one that will really be used as  the  MS(PC)-DOS  console driver.
        It  has  either of two bad effects, depending upon  which  driver  is
        specified first in CONFIG.SYS.  If ANSI.SYS is loaded  first,  memory
                                                      FANSI-CONSOLE                                                      _____________        is  consumed  by ANSI.SYS to no effect, since FANSI-CONSOLE  is  used
                                 FANSI-CONSOLE                                 _____________        instead of ANSI.SYS.  If FANSI-CONSOLE is loaded first, it won't work
        (unless /Y=1,  see the chapter entitled "Detailed Installation").  In
        this case,  ANSI.SYS  is  used  as  the  MS(PC)-DOS  console  driver.
        ANSI.SYS directly modifies ROM BIOS code variables (a bad programming
        practice) and then calls the  BIOS  expecting those variables to have
                                                               FANSI-CONSOLE                                                               _____________        some effect.  However, the BIOS calls are now calls to FANSI-CONSOLE,
        which doesn't  use  variables in the same place in memory as ANSI.SYS
        expected.






























        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                15        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                15








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly





        2.2.7 Restart MS(PC)-DOS        _____ _______ __________        2.2.7 Restart MS(PC)-DOS

                                            _______ __________        The seventh and  last  step  is  to restart MS(PC)-DOS.  Now that you
        have changed your CONFIG.SYS file, all you have to  do  is  use  that
        system disk when you turn on the computer or do a  Alt-Ctrl-Del.   Of
        course, you could have several system disks  with  both  FCONSOLE.DEV
                                                                  ___        and CONFIG.SYS on it and any one of them will do.  You do not need to
        have these files on an available  disk  drive  after  the  MS(PC)-DOS
                                                       FANSI-CONSOLE                                                       _____________        operating  system  is  loaded  at the start.   FANSI-CONSOLE  remains
        loaded in memory as part of the MS(PC)-DOS operating system until the
        next time you restart the system.

                    FANSI-CONSOLE                    _____________        You'll know FANSI-CONSOLE is installed  when  you see the single line
        banner with the name of the  program and our copyright message at the
        top of your screen when  you start.  If you don't see the banner when
                               FANSI-CONSOLE                               _____________        you start, you'll know FANSI-CONSOLE is  not  installed.   Simple  as
        that!  In  either  case,  you'll  see  the  old  familiar  MS(PC)-DOS
        prompt.

        Notice  that  we  don't  beat  you  over the head with a full  screen
        request for payment of the usage royalty,  like some programs do.  We
        just do that in the user manual!





























        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                16        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                16








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly





        2.2.8 Add BUFFERS=20 to CONFIG.SYS        _____ ___ __________ __ __________        2.2.8 Add BUFFERS=20 to CONFIG.SYS

        Although it is not necessary, you may also want to add something like
        the following line to the CONFIG.SYS file on your system disk:

             BUFFERS=20             BUFFERS=20

        The letters may be either upper or lower case.  The purpose  of  this
        command is to allow  more  buffer  space  for  MS(PC)-DOS  to use for
                                                                       FANSI-                                                                       ______        reading and writing files.  While this has  nothing to do with FANSI-
        CONSOLE        _______        CONSOLE, it will also speed up your computer by speeding up your disk
        accesses.  We  mention  it here because many people do not know about
        it.  The  only  negative aspect to using this line in your CONFIG.SYS
        file is that it consumes about 10KB of  read/write  memory  for extra
        buffer space which will no  longer  be available for your application
        programs.  However, you may replace the  number  20  with  a  smaller
        number, even one as small as 5. It will  still  speed up your system,
        although not  quite  as  much.  The space required is proportional to
        the number used.  Using a larger number may help  more  if you have a
        large or full hard disk.   If  the  number  is  too  large,  it  will
        actually start  slowing  the  computer down again.  Only you can find
        the best number for your system, but almost any number is better than
        the 2 you get by default.




























        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                17        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                17








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly





        2.2.9 Modify Prompt        _____ ______ ______        2.2.9 Modify Prompt

        Although it is not necessary, you  may want to add something like the
        following line to the AUTOEXEC.BAT file on your system disk:

        PROMPT $e[0m$e[J$n$g        PROMPT $e[0m$e[J$n$g

        Note  that  upper  and  lower  case letters must be used  exactly  as
        indicated in the prompt.  This is a MS(PC)-DOS  internal command that
        describes the prompt that MS(PC)-DOS should use  when it is ready for
        a new DOS command.  In this case,  we  have it send out an ANSI X3.64
        SGR  escape  sequence (indicated by the "$e[0m") to set  the  current
        screen colors and  other  attributes  to  the  normal  values  before
        displaying the  current  drive  letter ($n) and a greater than symbol
        ($g).  We also send  out  an  ANSI X3.64 ED escape sequence ($e[J) to
        erase the rest  of  the  screen  in the current colors.  We recommend
        this because some programs leave the current screen color  attributes
        in undesired states.

        However, using a prompt like this does  have some small side effects,
        which you should note.

          1.  The PROMPT only resets the  foreground  and  background  colors
              after every MS(PC)-DOS command, when the MS(PC)-DOS ECHO is ON.
              If ECHO is OFF, it has no effect.

          2.  The PROMPT resets the  foreground  and  background colors after
              _____              every MS(PC)-DOS command, when the MS(PC)-DOS ECHO is on.  This
              means that you  won't  be  able  to  change  the colors without
              changing the PROMPT, since it will reset them again immediately
              afterwards.  So you may want to experiment with  our many color
                    ______              files before setting up this PROMPT.

          3.  MS(PC)-DOS is apparently counting the prompt characters, except
              the  escape.   When you  use  this  prompt  and  you  type  the
              line-delete character (ESC for PC-DOS and Ctrl-X for MS-DOS) to
              restart a  line  that  you are typing at the MS(PC)-DOS prompt,
              MS(PC)-DOS spaces  over  too  far for the new line.  It doesn't
              realize that these prompt characters do not all  really  appear
              on the screen.

          4.  When    you    use    this    prompt   and   you    type    the
              echo-console-onto-printer character (Ctrl-PrtSc  for PC-DOS and
              Ctrl-P for  MS-DOS),  prompts do not appear the same as they do
              on the screen.  This is because your printer doesn't understand
              ANSI X3.64 escape sequences.





        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                18        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                18








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly


        You may find a different set of  colors or attributes desirable.  You
        may  also  want  the  DOS  prompt  to  use  different colors or  have
        different attributes than what you type after it.  So you may want to
        use different ANSI X3.64 SGR commands, like the following:

        PROMPT $e[32m$e[J$e[1;36;40m$n$g$e[2;32m        PROMPT $e[32m$e[J$e[1;36;40m$n$g$e[2;32m
















































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                19        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                19








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly





        2.2.10 Provide memory for applications programs        ______ _______ ______ ___ ____________ ________        2.2.10 Provide memory for applications programs

                  FANSI-CONSOLE                  _____________        Although, FANSI-CONSOLE does not require much memory for  itself,  it
        does require some.   If  you've  made  ram-disks  or  print  spoolers
        consume  all  the extra memory you had before, then  you'll  need  to
        adjust these programs to use a bit less.  You'll need to  have  about
        the same amount of memory left over  for applications programs as you
        did before.  Otherwise programs will  run  out of room because you've
        left too little for them.  Sometimes  a  program  will  not  complain
        directly about  having  less  memory, instead it may start doing more
        disk accesses than before.  It may  do this either to load and reload
        overlays  or  to  spill  large  amounts  of data into and  out  of  a
        temporary disk file.

        This even happens on computers fully loaded with  memory.   Remember,
        what counts is the  not the total memory you have, but how much of it
        you've left for the applications programs.   To  find  out  how  much
        memory is left over for applications  programs,  use  the  MS(PC)-DOS
        CHKDSK command.  The last line printed is the amount of memory usable
        by applications programs.  We can't tell you exactly  how much you'll
        need,  since  it depends on what programs you run.   However,  nearly
        everyone should leave at least 128K.

                                           FANSI-CONSOLE                                           _____________        Many of the problems reported with FANSI-CONSOLE are simply  problems
        caused by lack of enough memory for  the application program.  If you
                                                            FANSI-CONSOLE                                                            _____________        have a problem with an  application  program  when  FANSI-CONSOLE  is
                                                  FANSI-CONSOLE                                                  _____________        installed and you think it was caused by  FANSI-CONSOLE,  one  way to
        check  whether  it  is  a  memory problem is to run  the  application
        program under the MS(PC)-DOS  DEBUG  program,  which  happens  to  be
                                       FANSI-CONSOLE                   FANSI-                                       _____________                   ______        approximately the same size as FANSI-CONSOLE.  Do  this  with  FANSI-
        CONSOLE        _______        CONSOLE uninstalled.  Thus, about the  same  amount of memory is left
        for the application program.  Just "DEBUG program.ext" and "G" to get
        it running, and "Q" from DEBUG when  the application program is done.
                                           FANSI-CONSOLE                                           _____________        If it does the same thing  as when FANSI-CONSOLE is installed, it's a
        "not enough memory" problem.
















        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                20        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                20








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly






                         FANSI-CONSOLE        _______________________________        2.3 How do I use FANSI-CONSOLE?


                             FANSI-CONSOLE                             _____________        Now that  you  have  FANSI-CONSOLE installed, you just proceed as you
                                                      FANSI-CONSOLE                                                      _____________        always do,  and  mostly  ignore the fact that FANSI-CONSOLE is loaded
                                 FANSI-CONSOLE                                 _____________        and  running.   When the FANSI-CONSOLE banner appears at the  top  of
        your screen when you start MS(PC)-DOS, many programs magically  paint
        the screen faster without your further  intervention.   All  that  is
        necessary for you to do now is to appreciate our efforts!

        As noted before, you may want to use the typeahead buffer  more  than
        before.  You may also want to  take advantage of the new special keys
        described here.

        Some more useful features are  described  in  the  chapters  entitled
        "Detailed Installation" and  "Advanced  Features", but you don't need
        to rush to those chapters yet.


        2.3.1 Using the Ctrl-F key

        Press the  Ctrl-F  key  to simply flush (empty) the typeahead buffer.
        The Ctrl-F is left in the buffer, but many  programs  ignore it or do
        something harmless.  If you find an application that  does  something
        dangerous with the Ctrl-F key, you may want to  try  the  Ctrl-S  key
        instead.


        2.3.2 Using the Ctrl-S key

        Press  the  Ctrl-S  key  to  flush the typeahead buffer and,  if  the
        current program uses Ctrl-S as a pause key, cause the current program
        to  pause.   Most  programs  pay attention to  this  key  and  pause.
        Otherwise  they  probably ignore it.  The  standard  IBM-PC  software
        processes  the  Ctrl-S  slightly  differently,  by  not flushing  the
        typeahead buffer when  a  Ctrl-S  is  pressed.   This  means that the
        standard IBM-PC software ignores the Ctrl-S character if you  already
        have some characters in the typeahead  buffer.   For  other  ways  to
        pause, see the  description  of  the  Ctrl-Num-Lock  key  in the next
        paragraph and  of  the  /L=1 option in the chapter entitled "Detailed
        Installation".









        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                21        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                21








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly




        2.3.3 Using the Ctrl-Num-Lock key

        Press  the  Ctrl-Num-Lock key to cause the display to  pause  without
                                               FANSI-CONSOLE                                               _____________        flushing the typeahead buffer.   With  FANSI-CONSOLE  this key stroke
        combination works in a  manner  similar  to the way it works with the
        standard IBM-PC software.  One advantage, however, is that unlike the
                                   FANSI-CONSOLE                                   _____________        standard IBM-PC software,  FANSI-CONSOLE  prevents  the appearance of
        duplicate lines during a pause.   Press  any other key combination to
        unlock the pause.  Unless the second key combination  is a Ctrl-Break
        or a Ctrl-C, it  is  ignored  other than for clearing the pause.  Any
                                FANSI-CONSOLE                                _____________        program that works with FANSI-CONSOLE pauses with Ctrl-Num-Lock.  For
        other  ways to pause, see  the  description  of  the  Ctrl-S  in  the
        previous  paragraph  and of the /L=1 option in the  chapter  entitled
        "Detailed Installation".


        2.3.4 Using the Ctrl-C or Ctrl-Break keys

        Press the Ctrl-C key  to  cancel  most  programs.   It  is treated by
        FANSI-CONSOLE        _____________        FANSI-CONSOLE as equivalent to the Ctrl-Break  key.   They  are  both
                                                                FANSI-CONSOLE                                                                _____________        treated the way  the  standard IBM-PC software (without FANSI-CONSOLE
        installed) treats the Ctrl-Break key, which is to flush the typeahead
        buffer before placing a Ctrl-C  in  it.  The standard IBM-PC software
        processes  the  Ctrl-C  slightly  differently,  by  not flushing  the
        typeahead buffer when  a  Ctrl-C  is  pressed.   This  means that the
        standard  IBM-PC  software  ignores   the  MS(PC)-DOS  Ctrl-C  cancel
        character when you already have  some  characters  in  the  typeahead
        buffer.  Pressing Ctrl-C does not cancel any program that  Ctrl-Break
                                FANSI-CONSOLE                                _____________        does not cancel without FANSI-CONSOLE installed.


        2.3.5 Using the Ctrl-Equals key

        Press the Ctrl-Equals key combination,  instead  of  the  Ctrl-6  key
        combination used by the IBM-PC ROM BIOS, to get a Unit Separator (US)
        character.  Wherever any application program specifies the use of the
        Ctrl-6 key combination in its user manual,  use  Ctrl-Equals  instead
             FANSI-CONSOLE             _____________        when FANSI-CONSOLE is installed.  This is the  only  character  whose
                                          FANSI-CONSOLE                                          _____________        key combination is different with FANSI-CONSOLE than with the  IBM-PC
        ROM BIOS.  This character was placed at a different key in  order  to
                                                                       FANSI-                                                                       ______        free a whole row of keys (Ctrl-1 thru Ctrl-0) for later use by FANSI-
        CONSOLE        _______        CONSOLE.










        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                22        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                22








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly




        2.3.6 Using the Shift-PrtSc key

        Press  the  Left-Shift-PrtSc  key  combination  to  cause the  screen
                                            FANSI-CONSOLE                                            _____________        display  to  be  printed.    With   FANSI-CONSOLE   this  key  stroke
        combination works in the same manner as it  works  with  the standard
                                        FANSI-CONSOLE                                        _____________        IBM-PC software.  However, with FANSI-CONSOLE  the  Right-Shift-PrtSc
        key combination  does  not cause the screen display to be printed, as
        it would  with  the standard IBM-PC software.  This is to prevent the
        printing action from happening by  accident  when using the PrtSc key
        to generate an asterisk.










































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                23        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                23








        FANSI-CONSOLE (tm)                                   Starting Quickly        _____________ ____        FANSI-CONSOLE (tm)                                   Starting Quickly






                               FANSI-CONSOLE        _____________________________________        2.4 How do I uninstall FANSI-CONSOLE?


        If you ever  find  that  you  need to use another application program
                       FANSI-CONSOLE                       _____________        without having FANSI-CONSOLE installed, because of incompatibility or
        other reasons, it is just as easy to uninstall  as  it is to install.
        The easiest way is to  start your system using a system disk on which
        FANSI-CONSOLE        _____________        FANSI-CONSOLE is not installed.

        Another way is to simply remove the "DEVICE=FCONSOLE.DEV"  line  from
        the CONFIG.SYS file on  your  normal  system disk.  If it is the only
                                 FANSI-CONSOLE                                 _____________        line in CONFIG.SYS, then FANSI-CONSOLE may  also  be  uninstalled  by
        deleting  or  renaming CONFIG.SYS to another  name  like  CONFIG.TMP.
        Once the line is removed from CONFIG.SYS, or CONFIG.SYS is removed or
        renamed,  you  must  restart  your computer.  This  may  be  done  by
        pressing Alt-Ctrl-Del or by turning your computer off and then on.

        Simply removing FCONSOLE.DEV from your system disk, or  renaming  it,
        and restarting your computer also works, but it  causes the following
        error message to  be  displayed  by  MS(PC)-DOS  when  you start your
        computer:

             Bad or missing FCONSOLE.DEV             Bad or missing FCONSOLE.DEV

                                    FANSI-CONSOLE                                    _____________        If  you  are  uninstalling  FANSI-CONSOLE,  and  you  have  set  your
        MS(PC)-DOS prompt to use ANSI X3.64 escape sequences  codes, you will
        probably  want  to  replace  the  "DEVICE=FCONSOLE.DEV"  line in  the
        CONFIG.SYS file with a line containing "DEVICE=ANSI.SYS", or at least
        change your prompt again.





















        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                24        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                24








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation








                                      Chapter 3                                      Chapter 3

                                Detailed Installation                                Detailed Installation




        ___________________________________________________        3.1 So what is an MS(PC)-DOS device driver, anyway?


        Now  we  describe  some  features of MS(PC)-DOS  that  are  not  well
        described in  the  IBM-PC DOS manuals.  Some but not all the features
        are in the manuals, and what is there is  definitely  hard  to  find.
        IBM has even moved most of this information to a separately purchased
        manual called the DOS Technical Reference  Manual.   We  feel  it  is
                                                         FANSI-CONSOLE                                                         _____________        useful for  you  to know this to understand what FANSI-CONSOLE is and
        how it works.

        MS(PC)-DOS has  provision  for  people other than IBM or Microsoft to
        write something called a "loadable device driver".  A loadable device
        driver is Microsoft's excellent answer  to  the  problems  that  many
        IBM-PC compatible add-on hardware manufactures had with DOS 1.xx. The
        problem was that to make  a new piece of hardware work in your system
        as though it was really an integral part of the original  IBM-PC  and
        IBM-PC DOS, the add-on manufacturers had to create software for their
        cards  and  make  it  look  like  part  of  the original IBM-PC  DOS.
        However, they were not given the source program  code for MS(PC)-DOS,
        nor were they given a standard way to write their software  and  have
        MS(PC)-DOS  include  this  code  into  itself  as it started up.   So
        everyone started disassembling  the  operating system and making some
        very ugly programs that patched themselves into the operating  system
        in whatever ways they could figure out.  The result was that choosing
        two  of  these programs for two different pieces of  add-on  hardware
        would almost invariably cause  conflicts  and  they  would  not  work
        together.   Furthermore,  the  programs  would  not  work with  newer
        versions  of  MS(PC)-DOS, if  for  no  other  reason  than  that  the
        MS(PC)-DOS internal program variable addresses would change.

        Microsoft's solution was to  allow  add-on  hardware manufacturers to
        write  programs  called  loadable  device  drivers  to control  their
        hardware ("drive their devices") by following a standard  form  which
        Microsoft specified.  These device drivers are then loaded  at  start
        up time in a manner similar  to the original device drivers that come
        with  MS(PC)-DOS   from  your  original  manufacturer  (IBM  or  your
        equivalent maker).  This is a new feature provided by MS(PC)-DOS 2.00
        and later versions.


        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                25        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                25








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation


        Now all the add-on hardware manufacturers have to  do  is  to provide
        you with a driver program in  a regular MS(PC)-DOS file, and tell you
        how to include it in your operating system as you start up.  IBM even
        provided two loadable device drivers themselves.  One  is  a  console
        driver called  ANSI.SYS  and  was provided in object form.  The other
        was a read/write memory based disk  emulation  (ram-disk)  which  was
        provided as a listing (source form) in the DOS manual.

        The  best  part  is  how you incorporate  such  device  drivers  into
        MS(PC)-DOS.  All  you  have to do is provide a file called CONFIG.SYS
        with  a  few commands in it.  MS(PC)-DOS always read  this  file,  if
        there is  one  on  your  system  disk, when it starts and it executes
        these commands before  it  does  anything  else.   It  does this even
        before doing the AUTOEXEC.BAT file.   Because  of the nature of these
        commands, they may only be done in the  CONFIG.SYS  file  and nowhere
        else.

        The command to load a loadable device driver is:

        DEVICE=<driver file name> <options>        DEVICE=<driver file name> <options>

        The <driver file name> part is just the MS(PC)-DOS file name that the
        device  driver  object is to be found in.  What  the  <options>  part
        really needs to look like is entirely up to your device driver author
        (that's us!), and so looks like whatever they decide.  So it may look
        different  for  different  kinds  of  drivers.   Often <options>  are
        unnecessary.

        The order  of  the  DEVICE commands determines which is loaded first.
        If two drivers have the same name, like CON: which is the name of the
        MS(PC)-DOS console driver, the one which is loaded  last  is  the one
        that is really used.






















        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                26        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                26








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation






        _________________________________________        3.2 What if my computer is ... different?


        FANSI-CONSOLE        _____________        FANSI-CONSOLE  has  several  installation  options.   They  all  have
        default values which are set  for  standard  IBM-PC  display  adaptor
                           FANSI-CONSOLE                           _____________        cards,  so   that  FANSI-CONSOLE  should  work  on  all  "equivalent"
        computers and  cards.   However, if you do not have a standard IBM-PC
                              FANSI-CONSOLE                              _____________                    ______        display adapter card, FANSI-CONSOLE will probably work better if  the
        option values  are  changed.  You don't need to be a technical genius
        to figure  out  how  to  set  the options for your computer.  It just
        takes some reading, some thought, and a few  minutes  time.   It only
        needs to be figured out once, unless  you change your display adaptor
        card.  You will probably  find  that  it  will  be  worth the effort.
        Don't worry.  You can't  hurt  your  computer  by  experimenting  and
        trying out different  option  settings,  even  if they turn out to be
        wrong for your display adapter card.   The  worst  thing  that  could
        happen is that you would have to  start the installation process over
        again.

        The options are set by "parameters" which are added to the end of the
        DOS configuration command in the CONFIG.SYS file.  Each option  takes
        the form of an arbitrary number of spaces followed by one slash (or a
        minus sign, if you prefer) a letter, an equal sign, and a number.  If
        the number starts with a zero, it is considered to be  a  hexadecimal
        number.  Otherwise it is considered a  decimal  number.   The  letter
        tells which option is being set and the number specifies the value of
        the option.  It does  not  matter  which  case  (upper  or lower) the
        letters are.  An example is:

        DEVICE=FCONSOLE.DEV  /G=400  /S=10000        DEVICE=FCONSOLE.DEV  /G=400  /S=10000

        We use many spaces between options in  this manual, only for clarity.
        You may use as many spaces as  you  like, or even no spaces.  The one
        exception  is  that  there  must  be  at  least  one space after  the
        FCONSOLE.DEV file name, if there  are  any  options  specified.   The
        options  are  processed in a left to right order, so if an option  is
        specified more than once, the rightmost  instance  will  be  the  one
        which has an effect.












        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                27        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                27








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation


        The option letters and their meanings are as follows:

        A - Attributes
        B - Blink
        C - Color What You Can
        F - Font Table Address
        G - Ctrl-G Bell Length
        H - Horizontal Retrace Delay
        I - Initialize with Internal Controller parameters
        K - Key Bell Frequency
        L - Lock on Scroll-Lock
        M - Memory Allocated
        N - No Color Display
        O - One Finger Typing
        S - Screen Save Timeout
        T - TTY ROM BIOS Calls Use ANSI X3.64
        V - Vertical Retrace Delay
        W - Word Wide Screen Move
        X - Extended Features
        Y - Yuck, You Should Be So Compatible

        The  following  subsections  describe  each  option  in detail.   The
        chapter   entitled   "Compatibility    and   Limitations"   indicates
        appropriate option selections for  various  hardware  configurations,
        when they differ from the defaults.



                                    A - Attributes                                    _   __________                                    A - Attributes

                                                FANSI-CONSOLE                                                _____________        This option specifies the response that FANSI-CONSOLE should give  to
                                                         FANSI-CONSOLE                                                         _____________        the ANSI  X3.64 device attributes (DA) command.  FANSI-CONSOLE treats
        this option as a two byte  number.  The high byte specifies the first
        value returned, and the low byte specifies the  second byte returned.
        This  is  easiest  to  understand  when  a  hexadecimal   number   is
                                                    FANSI-CONSOLE                                                    _____________        specified.  So  for example, /A=00100 makes FANSI-CONSOLE return 1;0,
        which is the response code for  a DEC VT101 terminal.  The default is
        /A=00000.  This may be changed  if  we get an official implementation
        number.  Setting this option is only important  if you have a program
        expecting to  talk  to a particular ANSI X3.64 terminal, and it wants
        the exact response of that particular terminal from the DA command.













        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                28        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                28








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation



                                      B - Blink                                      _   _____                                      B - Blink

                                       FANSI-CONSOLE                                       _____________        This option specifies whether  FANSI-CONSOLE  should  blink the video
        display  on  and off when scrolling the color display  in  the  25x80
        alphanumeric screen display mode.  It  has  no effect unless the /H=1
                                               FANSI-CONSOLE                                               _____________        option is used.  A value of /B=1 means FANSI-CONSOLE should blink.  A
                            FANSI-CONSOLE                            _____________        value of /B=0 means FANSI-CONSOLE should not blink.  Other values are
        ignored.  Blinking  the  screen  during scrolling allows the use of a
        faster scrolling routine that would otherwise cause snow on  monitors
        requiring the /H=1 option.   If  the  /H=1  option  must  be used, we
        recommend using /B=1 (or /W=1, if  possible)  because  otherwise  the
        scrolling will be too slow.  The drawback to blinking is that  it  is
        somewhat hard on  the  eyes.   However,  this is what the IBM-PC BIOS
        does, so it will appear "normal".  The default value is /B=1, because
        the IBM-PC color graphics card requires  the  /H=1  option.   Related
        options are /H, /V, and /W.

        For the IBM-PC color graphics adaptor, we recommend /B=1.



                                C - Color What You Can                                _   _____ ____ ___ ___                                C - Color What You Can

                                      FANSI-CONSOLE                                      _____________        This option specifies whether FANSI-CONSOLE should use the ANSI X3.64
        SGR current graphics rendition to color the characters written to the
                                                        FANSI-CONSOLE                                                        _____________        screen where possible.  A value of /C=1  means  FANSI-CONSOLE  should
                                                     FANSI-CONSOLE                                                     _____________        use the current SGR.  A value of  /C=0 means FANSI-CONSOLE should use
        IBM-PC ROM BIOS compatible coloring.  Other values are ignored.  This
        option gives  the  initial  value for the FANSI-COLOR mode, which may
        later be changed with the ANSI X3.64 FANSI-SM  and FANSI-RM commands.
        If the /C=1 option is used, many programs  which  would  display only
        white characters on  a  black  background  with  /C=0,  will  display
        characters in  the  current colors and attributes set by the the last
        ANSI X3.64  SGR  command  instead.  This would normally be the colors
        and attributes set by the MS(PC)-DOS PROMPT command.   To  accomplish
        this, /C=1 forces all screen display mode settings be modified to the
        equivalent colored variation, if there is one.  Also, /C=1 forces the
        primary graphics rendition to have the last foreground and background
        colors explicitly set with the  ANSI  X3.64 SGR command.  The default
        value  is  /C=0, because this is the IBM-PC compatible  setting.   We
        generally suggest /C=1, because it makes many programs use the colors
        you prefer instead of white on  black.  This option is related to the
        /N option, which has priority over this option.

        However,  there  may  be  a  few programs which do not  color  things
        reasonably when  /C=1.   Note  that  this  option  will  only  affect
        programs which normally unintentionally cause the colors to be  white
        on  black  as  a  side  effect of changing the screen  display  mode.
        Programs which intentionally set the foreground and background colors
        will not be affected.



        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                29        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                29








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation





                                F - Font Table Address                                _   ____ _____ _______                                F - Font Table Address

        This option  specifies  the offset in the ROM BIOS segment (F000:) of
        the  graphics  character   set.    The  default  offset  is  /F=0FA6E
        (hexadecimal), since this is the address in  the IBM-PC ROM BIOS.  If
        this value is not set appropriately, then the characters displayed in
            ________  ______  _______  _____        the graphics  screen  display  modes will appear to be strange shapes
        instead of characters.  This only  affects  graphics  screen  display
        mode characters  and not alphanumeric screen display mode characters.
                  not                  ___        This  is  not meant to provide a way to  create  alternate  character
        sets, but only to specify where  in the ROM the regular character set
        is  to  be found.  Alternate character sets for the  graphics  screen
        display modes may be specified in the usual manner.



                                G - Ctrl-G Bell Length                                _   ______ ____ ______                                G - Ctrl-G Bell Length

        This option specifies the duration of the Ctrl-G  bell.  The duration
        is specified as a delay loop count, so the exact delay  time  depends
        upon  how  fast your IBM-PC or equivalent runs.  For  the  IBM-PC,  a
        count of /G=4096 lasts about one  second.   The  default  is  /G=4096
        because that's the amount  of  time  used by the IBM-PC ROM BIOS.  We
        like our bells a bit shorter,  like that provided by /G=400.  If your
        computer  is  faster than an IBM-PC, you may want  to  increase  this
        number.  Specifying /G=0 turns off the Ctrl-G bell entirely.



                             H - Horizontal Retrace Delay                             _   __________ _______ _____                             H - Horizontal Retrace Delay

                                          FANSI-CONSOLE                                          _____________        This  option  specifies  whether  FANSI-CONSOLE  must  wait  for  the
        horizontal retrace signal on color graphics cards before  writing  to
        screen memory in the 25x80 alphanumeric screen display modes.  It has
                                                                       FANSI-                                                                       ______        no effect for monochrome display cards.  A value of /H=1 means FANSI-
        CONSOLE                                      FANSI-CONSOLE        _______                                      _____________        CONSOLE  must  delay.  A value of /H=0 means FANSI-CONSOLE  need  not
        delay.  Other values are ignored.  The default value is /H=1, because
        the  IBM-PC  color graphics card requires this delay or  else  "snow"
        (also known as hashing) appears when the screen  is  written  to (you
        may not mind  this  but  we  do).  If your add-on manufacture's color
        graphics card does not require a delay,  then using /H=0 will provide
        a much nicer and faster screen display.   Related options are /B, /V,
        and /W.

        For the IBM-PC color graphics adaptor,  we  recommend  /H=1.   For  a
        Tecmar Graphics Master, use /H=0.  For Compaq's or  Zenith 150's, use
        /H=0.




        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                30        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                30








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation



                  I - Initialize with Internal Controller Parameters                  _   __________ ____ ________ __________ __________                  I - Initialize with Internal Controller Parameters

                                          FANSI-CONSOLE                                          _____________        This  option  specifies  whether  FANSI-CONSOLE  should  use its  own
        internal parameter values for initializing  the  CRT  controller.   A
                               FANSI-CONSOLE                               _____________        value of  /I=0  means  FANSI-CONSOLE should use the table provided by
                                                 FANSI-CONSOLE                                                 _____________        the ROM BIOS.   A  value  of  /I=n means FANSI-CONSOLE should use its
                                                  FANSI-CONSOLE                                                  _____________        internal  table  number  n.   Currently,  FANSI-CONSOLE  has two  (2)
        internal tables.  An  internal  table  should  be used if you want to
        provide your own  initial  values  which  are  different  from  those
        provided by the ROM BIOS.  To  find the internal tables in a specific
                   FANSI-CONSOLE                   _____________        version of FANSI-CONSOLE, so that you may change the values, you must
        specify /I=1 and examine interrupt vector 01D hex.   The other tables
        follow  immediately  afterwards,  in  address increments of  40  hex.
        Generally, we recommend  that  you  only  use /I=0, unless you are an
        advanced user.  So the default value is /I=0.



                                K - Key Bell Frequency                                _   ___ ____ _________                                K - Key Bell Frequency

        This option specifies the frequency of the keyboard  buffer full bell
        and of keyclicks.  The frequency is specified  as a delay loop count,
        so  the  exact  frequency  depends  upon  how  fast  your  IBM-PC  or
        equivalent runs.  The default value is  /K=048  because  that  causes
        FANSI-CONSOLE        _____________        FANSI-CONSOLE's keyboard buffer full bell to sound similar to that of
        the IBM-PC ROM BIOS.  If your  computer is faster than an IBM-PC, you
        may want to increase this number.  The keyclick  sounds  may  be made
        louder    by    pressing    Ctrl-Alt-DarkPlus    and    quieter    by
        Ctrl-Alt-DarkMinus, just as is normal for Compaq machines.



                               L - Lock on Scroll Lock                               _   ____ __ ______ ____                               L - Lock on Scroll Lock

        This option specifies whether to  provide  a one-finger pause key.  A
                            FANSI-CONSOLE                            _____________        value of /L=1 means FANSI-CONSOLE must provide the  one-finger  pause
                                          FANSI-CONSOLE                                          _____________        key.   A  value  of  /L=0  means  FANSI-CONSOLE must not provide  the
        one-finger pause key.  The default value is /L=0, because this is the
        IBM-PC compatible setting.  This option gives the initial  value  for
        the FANSI-LOCK  mode,  which may later be changed with the ANSI X3.64
        FANSI-SM and FANSI-RM commands.

        To use the one-finger pause key when the /L=1 option is  used,  press
        the Scroll-Lock key without any shifting keys to cause the display to
        pause  without  flushing  the  typeahead  buffer.   This  key  stroke
        combination  works  slightly  differently  than   the   Ctrl-Num-Lock
        combination.   Unlike  Ctrl-Num-Lock, Scroll-Lock acts as  a  toggle.
        When the  Scroll-Lock  pause  is  on,  other keys may be used to type
        ahead without affecting the pause.   Pressing  Scroll-Lock  a  second
        time clears the pause.   You  will  probably  find  Scroll-Lock  more
        convenient than Ctrl-Num-Lock, mostly because  it's  a  "one  finger"
                                                  FANSI-CONSOLE                                                  _____________        pause key.  Any program that works  with  FANSI-CONSOLE  pauses  with

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                31        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                31








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation


        Scroll-Lock.  Pressing the Scroll-Lock key  with  a shift or Alt key,
        when the /L=1 option is used, has the same effect as Scroll-Lock does
        when the /L=0 option is used.  In other words,  it  sets  the  scroll
        lock bit for  use  by  the  application  programs,  such as Borland's
        Sidekick.  For other ways to pause, see the desciptions of Ctrl-S and
        Ctrl-Num-Lock in the chapter entitled "Starting Quickly".



                                 M - Memory Allocated                                 _   ______ _________                                 M - Memory Allocated

        This option specifies how  much  read/write  memory  to  reserve  for
        varying space requirements.  This memory  is  used  for  saving  ANSI
        X3.64 command parameters and  keyboard  key  replacement strings.  To
        estimate your requirements,  add  your total keyboard key replacement
        string lengths to your maximum keyboard key replacement  key  length.
        Then add  100  and  multiply  by  1.25. Remember that this is only an
        estimate.  You may be able to do  with  less  space.   The  value  to
        specify is measured in bytes.  The default value is /M=512.



                                 N - No Color Display                                 _   __ _____ _______                                 N - No Color Display

                                        FANSI-CONSOLE                                        _____________        This option specifies  whether  FANSI-CONSOLE should attempt to force
        most  programs  to  use  only  black  and  white   for  the  graphics
                                            FANSI-CONSOLE                                            _____________        rendition.  A value of /N=1  means  FANSI-CONSOLE should try to force
                                                                FANSI-CONSOLE                                                                _____________        only black and white to be used.  A value of /N=0 means FANSI-CONSOLE
        should allow the  use  of  color.   Other values are ignored.  If the
        /N=1 option  is  used, many programs which would use color with /N=0,
        will display characters in black and white  instead.   To  accomplish
        this, /N=1 forces all screen display mode settings be modified to the
        equivalent  monochromatic  variation, if there is  one.   Also,  /N=1
        forces the primary graphics rendition to have the last foreground and
        background colors explicitly set with the  ANSI  X3.64  SGR  command.
        The default value is /N=0, because  this  is  the  IBM-PC  compatible
        setting.  We generally suggest /N=0, unless  you  have  a  monochrome
        display connected  to  a color display adaptor and you find that some
        colored characters are not readable on your display.   This option is
        related to the /C option, which this  option has priority over.  This
        option gives the initial value for the FANSI-NOCOLOR  mode, which may
        later be changed with the ANSI X3.64 FANSI-SM and FANSI-RM commands.












        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                32        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                32








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation



                                O - One Finger Typing                                _   ___ ______ ______                                O - One Finger Typing

                              The option is the letter O

        This option specifies whether to allow one finger typing.  A value of
                   FANSI-CONSOLE                   _____________        /O=1 means FANSI-CONSOLE will toggle the  Alt,  Ctrl,  or  shift  key
        states  only  when you press the appropriate key, and  not  when  you
        release it.  This means that  you  remain Alt'ed, Ctrl'ed, or shifted
        until you press the key again.  This is provided for handicappers and
        others who find it impractical to press  multiple keys at once.  Note
        that in this situation, each shift key is a separate shift  lock  and
        both must be off to get  unshifted characters.  A value of /O=0 means
        FANSI-CONSOLE        _____________        FANSI-CONSOLE will toggle the Alt, Ctrl, or shift key state both when
        you press the appropriate key, and when  you release it.  The default
        value is /O=0, since this provides the normal behavior of keyboards.



                               S - Screen Save Timeout                               _   ______ ____ _______                               S - Screen Save Timeout

                                      FANSI-CONSOLE                                      _____________        This option specifies whether FANSI-CONSOLE  should  use  its  screen
        saver feature and  how  long  the  timeout should be.  The value used
        should be the number of 1/18.2 second  intervals to be counted before
        turning off all the display output.   If no keys are pressed or there
        is no output from a program using ROM BIOS calls or MS-DOS before the
        timeout,  the  console screen display is  automatically  turned  off.
        This is to  prevent  you  from  accidentally  permanently  burning  a
        pattern into your display screen by displaying  the same thing on the
        screen too long.  When the display is turned off, any key including a
        shifting key may be  pressed  to  turn the display back on.  When the
        display is turned back on, the  data displayed appears the same as it
        did just before  the  display  was  turned off.  The default count of
        /S=0 may be  used  to  specify  always keeping the screen display on,
        which is the behavior of the standard ROM  BIOS  software.   We don't
        recommend  this  setting, but we make the defaults as  compatible  as
        possible with the standard,  to  avoid  surprising people.  Otherwise
        the timeout can be as much as about one hour if /S=0FFFF is used.  We
        suggest /S=10000, for a timeout of about ten minutes.  18.2 units/sec
        * 60 secs/min * 10 min = 10920 units, actually.














        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                33        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                33








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation


        Note that some programs set the  border,  color  palette,  or  screen
        display mode directly rather  than  through  the  BIOS  calls.   Such
        programs include some painting programs,  like  PC  Paint,  and  some
        programs  which  use  more  than  one  screen display mode to  option
        between graphics  and  text,  like Lotus 123. When these programs are
        used  and  the screen is disabled and then restored,  the  border  or
        palette may be a different color than before the screen was disabled,
        or the screen may appear to be totally  distorted.   This  is because
        hardware state of these values cannot be  read and then restored, but
        they must be changed  to  disable  the screen.  So to do the restore,
        FANSI-CONSOLE        _____________        FANSI-CONSOLE must assume the values were as they  were  last  set by
        FANSI-CONSOLE        _____________        FANSI-CONSOLE.

        If you specify the /S option but the screen  does  not turn off after
        the specified  period,  then it may be that your display adaptor card
        has no way to disable video signal.   There  is no way to have the /S
        option work with such adaptors.  It may also be that the video signal
        disable  is  turned  off  in  a manner which is different  from  that
                                         FANSI-CONSOLE                                         _____________        required by IBM standard cards.  FANSI-CONSOLE may have  an  extended
        features option which  must  be  used  with such an adaptor.  See the
        description of the /X options below.



                        T - TTY ROM BIOS Calls Use ANSI X3.64                        _   ___ ___ ____ _____ ___ ____ _____                        T - TTY ROM BIOS Calls Use ANSI X3.64

        This option specifies whether the ROM BIOS  video call for TTY output
        (INT 10 hex with AH =  15 decimal) should process ANSI X3.64 standard
                                                 FANSI-CONSOLE                                                 _____________        escape sequences.  A value of /T=1 means FANSI-CONSOLE  will  process
        the ANSI X3.64 standard escape sequences  found  in  the  TTY  output
                                       FANSI-CONSOLE                                       _____________        calls.  A value of /T=0 means  FANSI-CONSOLE  will  process  the  TTY
        output calls in a manner compatible with the  IBM-PC  ROM  BIOS.  The
        default   value   is  /T=0.   We  generally   recommend   /T=0,   for
        compatibility.  With /T=1,  some  communications programs may be made
        to process ANSI X3.64 escape sequences properly, and  emulate an ANSI
        X3.64 standard terminal, even when those  programs  do  not  normally
        provide that as a feature.  Specifying /T=1 is only incompatible with
        a few programs which use the TTY call  to  display  IBM-PC characters
        with values less than the value of a space.















        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                34        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                34








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation



                              V - Vertical Retrace Delay                              _   ________ _______ _____                              V - Vertical Retrace Delay

                                          FANSI-CONSOLE                                          _____________        This  option  specifies  whether  FANSI-CONSOLE should wait  for  the
        vertical retrace  signal  to  be on before blinking the video display
        when scrolling the color display in  the  25x80  alphanumeric  screen
        display mode.  It has no effect for monochrome display cards.  It has
                                                   FANSI-CONSOLE                                                   _____________        no effect if /B=0.  A value of  /V=1 means FANSI-CONSOLE should wait.
                                 FANSI-CONSOLE                                 _____________        A value  of  /V=0  means FANSI-CONSOLE should not wait.  Other values
        are ignored.  If the /B=1 option must be  used,  /V=1  is recommended
        because it makes the blink  slightly  less annoying.  The drawback to
        waiting with /V=1 is that it  slows  the  scrolling  speed  slightly.
        However, this is what the IBM-PC ROM BIOS does,  so  it  will  appear
        "normal".   The  default  value  is  /V=1,  because /B=1 is also  the
        default.  Related options are /B, /H, and /W.

        For the IBM-PC color graphics adaptor, we recommend /V=1.

                              W - Word Wide Screen Move                              _   ____ ____ ______ ____                              W - Word Wide Screen Move

                                      FANSI-CONSOLE                                      _____________        This option specifies whether FANSI-CONSOLE should move a whole  word
        at a time after waiting for horizontal retrace.  It has no effect for
        monochrome display cards.  It has no effect if /H=0.  A value of /W=1
              FANSI-CONSOLE              _____________        means FANSI-CONSOLE should move  a  word  at a time.  A value of /W=0
              FANSI-CONSOLE              _____________        means FANSI-CONSOLE  should  move a byte at a time.  Other values are
        ignored.  If it does not cause  hashing (snow) on the screen, /W=1 is
        recommended because it makes the scrolling faster.  However, /W=0  is
        the default because  /W=1  causes  hashing  on  the  IBM-PC  graphics
        adaptor on  an  IBM-PC.   Generally, only machines with a 16-bit wide
        data  bus  and an 8086, 80186, or 80286 like the IBM-PC AT, the  AT&T
        PC, or DeskPro are fast enough for /W=1 to  not  cause snow.  On such
        machines /W=1 is usually slower  than  /B=0.  Related options are /B,
        /H, and /V.

                                    X - Extensions                                    _   __________                                    X - Extensions

                                        FANSI-CONSOLE                                        _____________        This  option  specifies whether FANSI-CONSOLE should  use  extensions
        which are peculiar to a particular display  adaptor.  A value of /X=0
        means use no extensions, and is therefore the  default.   A  value of
        /X=1 means use Zenith Z150/160 extensions.  A value of /X=2 means use
        Mad-1 extensions.  If /X=1 is not used for  a  Zenith  Z150/160, then
        using the /S option with a non-zero  value  will  not  turn  off  the
        screen display.  If /X=2 is  not used for a Mad-1, then the break key
        and  the  numeric pad comma key will be ignored.   Other  values  are
        currently ignored.   Other  /X  values may be added as extensions for
        one display adaptor are found  to  be incompatible with other display
        adaptors.   Check  the  FCONSOLE.HST  file  for  any  recently  added
        values.






        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                35        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                35








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation



                        Y - Yuck, You Should Be So Compatible                        _   _____ ___ ______ __ __ __________                        Y - Yuck, You Should Be So Compatible

                                        FANSI-CONSOLE                                        _____________        This option specifies  whether  FANSI-CONSOLE should be as compatible
                                                               FANSI-CONSOLE                                                               _____________        as it can  be  to  the  IBM-PC ROM BIOS.  In designing FANSI-CONSOLE,
        there were a few  tough  decisions  which  had  to  be made.  Certain
        programs directly  modify ROM BIOS screen variables themselves before
        making calls to ROM BIOS screen routines to make other changes.  This
        is not a proper way of doing things, because it violates the intended
        purpose  of  the  ROM  BIOS,  but some programs did it  anyway.   The
        practice is sometimes called "making endruns around the  BIOS".   The
        proper  way  is  to  make  calls to the appropriate ROM  BIOS  screen
        routines to make all the changes.

                                  FANSI-CONSOLE                                  _____________        The problem is that,  if  FANSI-CONSOLE  is to be fast and to provide
        several  of  the  new  features,  it  has  to  use it's own  internal
                                                                       FANSI-                                                                       ______        variables and not the ROM BIOS screen variables.   However, if FANSI-
        CONSOLE        _______        CONSOLE doesn't look at the ROM BIOS screen variables, these programs
        will not run correctly.  When these programs  run, it looks like most
        of the characters are overwritten, in the wrong place, and the screen
        is mostly empty.  So the choice is to be  fast,  or to be compatible.
        Since you may have already purchased some of these improper programs,
        we  feel  that we should leave the decision up to you, so we  provide
        the /Y option as a way for you to make this decision.

                                   FANSI-CONSOLE                                   _____________        A value of /Y=1 means that FANSI-CONSOLE  should start out being more
                                                           not                                                           ___        compatible  but  slightly   slower.    This  does  not  mean  totally
        compatible  (nothing  ever  could  be),  but  it's as close as  we've
        figured out how to be and still be fast.   This  also means that some
        of the extended features will be unusable.   Particularly,  it  means
        that only 8 screen pages may be used, and  that  the extended 50 line
        interlaced screen display modes may  not  be  used.   Currently,  the
        speed penalty is about  7%  at  most,  so you may not even notice the
        difference.  The penalty may become  greater  in later versions if we
        discover more things that may be done to increase compatibility.

                                       FANSI-CONSOLE                                       _____________        A value of  /Y=0  means  that  FANSI-CONSOLE  should  start out being
        faster  but  slightly  incompatible.   It also allows  some  extended
        features to be used.  This provides enough compatibility  to run most
        but not all  programs.   Using  this  mode  is  a  way  to  test  the
        portability of a program.  If it doesn't  run correctly in this mode,
        it may have problems running on some "almost  but  not  quite" IBM-PC
        equivalent machines.   Of  course, it does not mean that a program is
        portable just because it runs in this mode.










        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                36        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                36








        FANSI-CONSOLE (tm)                              Detailed Installation        _____________ ____        FANSI-CONSOLE (tm)                              Detailed Installation


        The default is /Y=1, since this provides  normal behavior for as many
        of your applications  as  possible.   Where  it is known that /Y=1 is
        required  for  a specific program, it is noted in  the  compatibility
                FANSI-CONSOLE                _____________        lists.  FANSI-CONSOLE also provides the Alt-Ctrl-Down key combination
        and  the  FANSI-SM  command  to  option  to  the  /Y=1 mode, and  the
        Alt-Ctrl-Up key combination and the FANSI-RM command to option to the
        /Y=0 mode at any later time.  This option gives the initial value for
        the FANSI-CMP mode, which may later be changed  with  the  ANSI X3.64
        FANSI-SM and FANSI-RM commands.













































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                37        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                37








        FANSI-CONSOLE (tm)                             Programming Background        _____________ ____        FANSI-CONSOLE (tm)                             Programming Background








                                      Chapter 4                                      Chapter 4

                                Programming Background                                Programming Background




        _______________________________________        4.1 Which screen access method is best?


        This chapter is devoted to a discussion  of screen and keyboard usage
        methods  and  their  portability  to  other  computers.   It  is   an
        introduction for the next two chapters, to help you decide which type
        of screen access to use in your programs.  You do not need to read it
        unless you are going to write programs  for your computer.  You might
        want  to  read  it  anyway, if you are curious, since it is  not  too
        technical.

        There are three general ways to access the screen and keyboard:

          1.  Direct hardware manipulation.

          2.  ROM BIOS calls.

          3.  MS(PC)-DOS calls.

        Each has its own advantages and disadvantages.   As you move down our
        list above, the methods generally become  somewhat  slower  and  less
        versatile but they also become  more  computer  independent.   It  is
        probably obvious why  you  would  want  your  programs  to access the
        screen as fast as possible.  What may not be obvious is why you might
        want them to be computer independent.

        The more  computer  independent a program is, the more likely it will
        be that that program will run on your particular computer.  Sure, you
        bought your IBM-PC or equivalent because it  is (or is equivalent to)
        what everyone else  is  buying.   We  are sure you have heard stories
        from friends  about  how  great  some  IBM-PC card was but it was not
        "IBM-PC compatible".  By the  way,  we  like  the  word  "equivalent"
        better  than  "compatible", when used in this context.  We  are  also
        sure that you have at one time or another heard other  stories  about
        how badly designed parts of the IBM-PC are.  Not that we  agree  with
        all such complaints.  The problem is that it is impossible to improve
        on  IBM's  ideas if everything has to be the same as IBM's!  So  pick
        one, please.  Which will it be: "equivalent" or  "better than IBM's"?
        Well, if more programs used  more  computer  independent  methods  to
        access the hardware on your IBM-PC,  you could have your cake and eat

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                38        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                38








        FANSI-CONSOLE (tm)                             Programming Background        _____________ ____        FANSI-CONSOLE (tm)                             Programming Background


        it too.

        For example, consider that many programs use the  first screen access
        method: direct hardware manipulation.  If someone (even IBM) designed
        a hot new video board for the IBM-PC that  allowed  you to display 80
        lines of 132 columns of text,  none of these programs would work with
        this board.  In fact, there are some boards out  there  that  can  do
        something  like  this,  and  some  are  not much more expensive  than
        IBM's!  So you paid a high price for all  the  speed of direct screen
        access: you must buy an equivalent board.

        If the same programs  instead  called  the  ROM BIOS or the DOS to do
        screen accesses, all  that  would  be  needed is for the screen board
        manufacturer to provide  a  replacement  for  part of the ROM BIOS or
        part of MS(PC)-DOS for screen access.

        It  turns  out that the IBM-PC ROM BIOS is  slow.   Since  MS(PC)-DOS
        calls also call the IBM-PC ROM BIOS, they are also slow.  Anyway, the
        price for  computer  independence is much higher than it needs to be.
                                     FANSI-CONSOLE                                     _____________        How do we know?  That's what FANSI-CONSOLE is all about!  It replaces
        IBM-PC ROM BIOS code  for  the  screen and keyboard with our own BIOS
        code.  The  result  is that programs which use the BIOS or MS(PC)-DOS
        calls for screen access are speeded up.

        It  also  did  not  help that most of the things that could  be  done
        directly to the screen are not supported with some type of MS(PC)-DOS
        call.  This was  remedied  somewhat  with  the  introduction  of  the
        concept of an MS(PC)-DOS device driver.

        There are several  reasons  that  MS(PC)-DOS  calls  should  be  used
        instead of ROM BIOS calls, wherever feasible:

          1.  The  MS(PC)-DOS  calls   provide   some  functions  in  a  more
              convenient manner for the programmer than the  BIOS  does.   In
              particular, they are the easiest to  use  from  most  languages
              other than assembly language.

          2.  Program screen displays may  be  redirected  into an MS(PC)-DOS
              file instead  of  directed to the screen.  From there it can be
              manipulated just like any other data file.

          3.  The program may be used with the CTTY  program  on  an external
              terminal via your serial port.

          4.  Even more computers using MS(PC)-DOS  support  the  ANSI  X3.64
              standard through  MS(PC)-DOS  calls  than  those  supporting an
              equivalent to the IBM-PC ROM BIOS.  The interrupt vectors  used
              by the IBM-PC ROM BIOS standard violate Intel's reservation  of
              them  for  its  newer  processors  like  the 80186. So not  all
              computers   which  could  otherwise  be  equivalent  have   the
              possibility  of  using  these  vectors for screen  or  keyboard
              access.  So the program could be run  on more machines now, and
              in the future.

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                39        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                39








        FANSI-CONSOLE (tm)                             Programming Background        _____________ ____        FANSI-CONSOLE (tm)                             Programming Background



        Remember though, that the price we pay  for portability is some speed
        and some versatility.  But the price does  not have to be unbearable,
                   FANSI-CONSOLE                   _____________        if you use FANSI-CONSOLE.


















































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                40        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.                40








        FANSI-CONSOLE (tm)                      Compatibility and Limitations        _____________ ____        FANSI-CONSOLE (tm)                      Compatibility and Limitations








                                      Chapter 8                                      Chapter 8

                            Compatibility and Limitations                            Compatibility and Limitations




                                  FANSI-CONSOLE        _____________________________________________        8.1 What limitations does FANSI-CONSOLE have?


        FANSI-CONSOLE        _____________        FANSI-CONSOLE does have some limitations and we hope  to remedy these
        in the future.

        FANSI-CONSOLE        _____________        FANSI-CONSOLE  could  easily  be  made to accept  more  of  the  ANSI
        standard escape sequences.  We will try to extend it.

        FANSI-CONSOLE        _____________        FANSI-CONSOLE  may  not  work  with some key  reassignment  programs.
        Because the typeahead buffer is bigger, it must be put in a different
        place.  We will try to  make it work with most of these programs, and
        try to eliminate the need for separate key  reassignment programs, by
                            FANSI-CONSOLE                            _____________        adding functions to FANSI-CONSOLE, or to a companion program.

        FANSI-CONSOLE        _____________        FANSI-CONSOLE may not work with  some  mouse drivers.  However, it is
        compatible with the most popular mice.

        FANSI-CONSOLE        _____________        FANSI-CONSOLE may not work with newer IBM graphics adaptors.  We will
        provide either separate versions or appropriate switches.





















        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               130        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               130








        FANSI-CONSOLE (tm)                      Compatibility and Limitations        _____________ ____        FANSI-CONSOLE (tm)                      Compatibility and Limitations






                                          FANSI-CONSOLE        ________________________________________________        8.2 Are there several versions of FANSI-CONSOLE?


        FANSI-CONSOLE        _____________        FANSI-CONSOLE has at least three  different  versions  for  differing
        kinds of machines.  The type of machine which a version is  meant  to
        run on is indicated by the first character of the serial number:

        0                IBM-PC and very compatibles with very compatible ROM
                         BIOS.  This includes the IBM-PC  AT.  The  ROM  BIOS
                         must have console variables in the same place as the
                         IBM-PC.

        1                Computers with  IBM-PC  work-alike  display adaptors
                         and keyboards.  No ROM BIOS is expected, and if  one
                         exists, it is ignored.



































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               131        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               131








        FANSI-CONSOLE (tm)                      Compatibility and Limitations        _____________ ____        FANSI-CONSOLE (tm)                      Compatibility and Limitations






                                              FANSI-CONSOLE        ____________________________________________________        8.3 What programs are compatible with FANSI-CONSOLE?


        Any program which only uses DOS or ROM BIOS screen and keyboard calls
                         FANSI-CONSOLE                         _____________        should work with FANSI-CONSOLE, and have faster screen painting.  Any
        compiler  or  assembler  should  work.   Programs  written which  use
        standard language calls for reading and writing  the  console  should
        have faster  screen painting.  Only programs that manipulate hardware
        address contents or BIOS variables directly  may  not  run  correctly
             FANSI-CONSOLE             _____________        with FANSI-CONSOLE.

        The indication "(faster)" in the list below means  that the program's
                                                   FANSI-CONSOLE                                                   _____________        screen writing  is noticeably faster using FANSI-CONSOLE than without
        using it,  or,  for  compilers, that programs written in the language
        have faster screen writing.  Other  programs  listed work at the same
        speed as they would otherwise or  we just haven't done a benchmark to
        find out otherwise.

                                                                       FANSI-                                                                       ______        The indication  "/Y=0"  means that the program may be run with FANSI-
        CONSOLE        _______        CONSOLE with either /Y=0 or  /Y=1.   The indication "/Y=1" means that
                                        FANSI-CONSOLE                                        _____________        the program  must  be  run with FANSI-CONSOLE in it's most compatible
        mode.  For other programs we do  not know whether /Y=0 will work, but
        /Y=1 does work.



























        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               132        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               132








        FANSI-CONSOLE (tm)                      Compatibility and Limitations        _____________ ____        FANSI-CONSOLE (tm)                      Compatibility and Limitations


                                                             FANSI-CONSOLE                                                             _____________        This list of programs we believe are compatible with FANSI-CONSOLE is
        not all inclusive by any means!

        (Names below are all trademarks of indicated companies)

        Application Executive Corporation - APX Core Executive (faster)
        Ashton-Tate - DBase II (/Y=1)
                DBase III
                Framework
        BACKSCRL.COM
        Borland International - Sidekick
        Buttonware - PC-FILE (faster) (/Y=0)
        Columbia University - Kermit (faster)
        Computer Innovations - C86 C compiler, all versions (faster)
        CompuView - Vedit - IBM-PC version (some things faster)
                Vedit - MS-DOS version (faster)
        Condor Computer - Condor (faster)
        Consortium Software, UofM - ABC
        Davong - Multi-OS (faster)
        Decision Resources - Chart-Master 6.03 (faster)
        Emerging Technologies - Edix
        Forth, Inc. - PolyForth II (faster)
        Gersbach, Jack - DOSEDIT1 (/Y=1)
                DOSEDIT2 (/Y=1)
        Hayes - SmartCom
                                  FANSI-RAMDISK                                  _____________        Hersey Micro Consulting - FANSI-RAMDISK (/Y=0)
                MODEM86                _______                MODEM86 (faster) (/Y=0)
        IBM - Basic, all versions (faster) (/Y=0)
                DOS Command Retriever (/Y=1)
                IBM-PC DOS 2.00 (faster) (/Y=0)
                IBM-PC DOS 2.10 (faster) (/Y=0)
                IBM-PC DOS 3.00 (faster) (/Y=0)
                Personal Editor
                TopView, preliminary
                WordProof (/Y=0)
                Utilities - Dos command retriever (/Y=1)
        IUS - Accounting Series - General Ledger (faster) (/Y=0)
        Lattice - C compiler, all versions (/Y=0)
        Lifetree Software - Volkswriter
        Logitech - Modula II
        Lotus Development Corp. - Lotus 1-2-3
                Symphony
        Mansfield Software - Kedit
        Mark of the Unicorn - Final Word MS-DOS version (faster)
        MetaSoft - Benchmark
        Micrografx, Inc. - PC-Draw (faster)
        MicroPro - Wordstar IBM-PC version
        Microsoft - Assembler (/Y=0)
                C compiler (faster) (/Y=0)
                Mouse (/Y=1)
                Multiplan MS-DOS version (faster) (/Y=0)
                Pascal Compiler (faster) (/Y=0)
                Project

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               133        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               133








        FANSI-CONSOLE (tm)                      Compatibility and Limitations        _____________ ____        FANSI-CONSOLE (tm)                      Compatibility and Limitations


                Word 1.1
        Microstuf - Crosstalk
        MORERAM -
        Mouse Systems - PC Mouse
                PC Paint
        Norton - Norton Utilities 2.0 (faster) (/Y=0)
                Norton Utilities 3.0 (faster if not direct I/O) (/Y=0)
        QMODEM -
        Quarterdeck - DESQ
        RoseSoft - Prokey (except LAYOUT program) (/Y=0)
        SAMNA Corporation - SAMNA Word (faster)
        Satellite Software International -
                (use Ctrl-Equals instead of Ctrl-6)
                - P-Edit
                - Word Perfect
        Sorcim - SuperCalc (faster)
        Tall Tree Systems - J-Drive
                J-Spool
        Tandy - Teleterm (faster)
        Thesys - TMS Fastware
        University of Michigan - Window (/Y=0)
        Zenith - GWBasic (/Y=1)
        Zsoft Corp - PC Paintbrush































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               134        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               134








        FANSI-CONSOLE (tm)                      Compatibility and Limitations        _____________ ____        FANSI-CONSOLE (tm)                      Compatibility and Limitations






                                               FANSI-CONSOLE        _____________________________________________________        8.4 What computers are compatible with FANSI-CONSOLE?


        This list of  computers  and  display  adaptor  cards  we believe are
                        FANSI-CONSOLE                        _____________        compatible with FANSI-CONSOLE is not all inclusive by any means!

        (Names below are all trademarks of indicated companies)

        Amdek - MAI (/H=0)
        AT&T - 6300 (/H=1/W=1/B=0/V=0)
                (Except keyboard status lights not supported yet)
        Columbia Data Products - Multi Personal Computer
        Compaq - Compaq (/H=0)
                Compaq Plus (/H=0)
                Compaq Deskpro (/H=0)
        Data General - One (has no video disable)
                (No support yet for extra keys)
                (Some problems with mode changes)
        Everex - Graphics Edge (/H=0)
                (Use all 3 jumpers ON, card has no video disable)
        Hercules - B&W Graphics Card
                (no support for graphics modes or second page)
        IBM - PC, 64K motherboard
                PC, 256K motherboard
                PC/XT
                Portable PC
                PC/AT
                Monochrome display adaptor
                Color graphics display adaptor (/H=1)
        Leading Edge - Leading Edge PC
        Mad Computer - Mad-1 (/X=2)
        Paradise - Modular Graphics (/H=0)
        Plantronics - Color Plus (/H=1)
        QuadRam - QM2
        Tandy - Tandy 1000 (extra keys not supported yet)
                Tandy 1200 (extra keys not supported yet)
        Tecmar - Graphics Master (/H=0)
        Zenith - Z150 (/X=1/H=0)
                Z160 (/X=1/H=0)
        If a card has no video disable, then the screen save  feature  cannot
        be made to work.









        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               135        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               135








        FANSI-CONSOLE (tm)                      Compatibility and Limitations        _____________ ____        FANSI-CONSOLE (tm)                      Compatibility and Limitations






                                                FANSI-CONSOLE        ______________________________________________________        8.5 What programs are incompatible with FANSI-CONSOLE?


        The following are some areas of expected incompatibility problems:

          1.  Programs which replace the keyboard interrupt vectors may cause
                                  FANSI-CONSOLE                                  _____________              some difficulty for FANSI-CONSOLE or vice versa.

          2.  Programs  which  try  to  insert characters into  the  keyboard
                                                 FANSI-CONSOLE                                                 _____________              typeahead buffer may not work with FANSI-CONSOLE.

          3.  Some programs that manipulate BIOS variables directly.

          4.  DOS versions earlier  than  DOS  2.00  do  not  have a standard
              mechanism  for  installing  loadable  device  drivers.   It  is
              conceivable that  if  there  is enough demand, a version may be
              made for earlier versions of  the  DOS.   However,  in  general
              other application packages  should  instead be upgraded to work
              with the current DOS (even if not to use new DOS features).  In
              most cases other application products need no upgrading to work
              under the current DOS version.   In  other  cases  the  upgrade
              should be available for a small price.

          5.  Some programs that run from  an  AUTOEXEC.BAT  file  and  which
              cause the MS(PC)-DOS to redo  part  of  the  bootstrap  process
                    FANSI-CONSOLE                    _____________              after FANSI-CONSOLE has been initialized.  This is because they
                                          FANSI-CONSOLE                                          _____________              are reusing the memory that FANSI-CONSOLE resides in  while  it
              is  active  and  processing timer  interrupts.   Such  programs
              should be made into device drivers  and  placed  first  in  the
              CONFIG.SYS file, or be made to use INT 19.

          6.  Programs which do not work properly with  the  IBM-PC  ANSI.SYS
              driver.  Most of these kinds of  programs  work  for  the  most
              part, but some characters used in  display  messages  are  ANSI
              X3.64 control characters and therefore do not get displayed.

          7.  Programs which expect  all  MS(PC)-DOS  console input/output to
              eventually be done through the ROM BIOS, instead of directly by
              the MS(PC)-DOS console driver.











        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               136        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               136








        FANSI-CONSOLE (tm)                      Compatibility and Limitations        _____________ ____        FANSI-CONSOLE (tm)                      Compatibility and Limitations


        Please let us know about these programs  so  we  may  either  find  a
        solution for you and  others  in  the  same  predicament  or at least
        provide a more specific warning.  Since we may be able to  solve  the
        problem,  programs  may  move  from  this  list  to  the  one  above.
        Sometimes we leave them in this list, but provide a patch which makes
                                                          FANSI-CONSOLE                                                          _____________        specific versions of the programs below work with FANSI-CONSOLE.

                                                                FANSI-CONSOLE                                                                _____________        This list of programs we believe are incompatible with  FANSI-CONSOLE
        is not all inclusive by any means!

                                                    FANSI-CONSOLE                                                    _____________        Programs we believe are NOT compatible with FANSI-CONSOLE:

        (Names below are all trademarks of indicated companies)

        CGCLOCK -
        DDATE - Works but arrow characters displayed are
                ANSI control characters.
        IBM - IBM-PC DOS 1.0 -
                Does not allow loadable device drivers.
        IBM - IBM-PC DOS 1.1 -
                Does not allow loadable device drivers.
        KeyNote -
        Mark of the Unicorn - PC/InterComm -
                Replaces keyboard BIOS.
        REMIND - Causes "missed characters".
        RoseSoft - Prokey -
                Everything but Prokey LAYOUT program works.
                LAYOUT requires ROM BASED BIOS keyboard handlers.
        SCRLLOCK -
                                               FANSI-CONSOLE                                               _____________                Equivalent function already in FANSI-CONSOLE.
        SCRNSAVE -
                                               FANSI-CONSOLE                                               _____________                Equivalent function already in FANSI-CONSOLE.
        Seasoned Systems - Dvorak keyboard program.
                                               FANSI-CONSOLE                                               _____________                Equivalent function already in FANSI-CONSOLE.
        Software Link - MultiLink
                Expects MS(PC)-DOS console output to all go through
                the ROM BIOS.
        STB - PC Accelerator -
                Doesn't go thru reboot.  Not well investigated
                yet.
        Xywrite -
                Reported that it only works when BREAK=OFF.
                Not well investigated yet.











        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               137        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               137








        FANSI-CONSOLE (tm)                      Compatibility and Limitations        _____________ ____        FANSI-CONSOLE (tm)                      Compatibility and Limitations






                                                 FANSI-CONSOLE        _______________________________________________________        8.6 What computers are incompatible with FANSI-CONSOLE?


        For some computers, there are currently some general problems we know
        which may prevent portability to computers other than IBM-PC's.

              FANSI-CONSOLE              _____________          1.  FANSI-CONSOLE always resides in memory.  Although it is  not  a
              big program, it may be big  enough to cause problems on a small
              system (192K or less) with  at  least  some  other  application
              programs not  having enough remaining memory.  Also using other
              memory resident programs, even on  larger  systems,  may  cause
              memory  space  problems, but these are  often  solvable.   Such
              memory resident programs include  ram-disks and print spoolers.
              One simple solution for problems related to these  programs  is
              to  reduce  their memory usage a bit.  Of course,  it  is  also
              usually possible to eliminate the problem by buying more memory
              for your computer.   In  these  cases,  just one bank of 64K is
              much more than enough.

          2.  The location of keyboard ROM BIOS variables must be the same as
                                        FANSI-CONSOLE                                        _____________              the IBM-PC's in order for FANSI-CONSOLE to support  some of the
              fancier keyboard reassignment programs.  We will have a version
                 FANSI-CONSOLE                 _____________              of FANSI-CONSOLE for machines with slightly less compatible ROM
              BIOSes.

          3.  The  location  of  the  lower  half of the font table  for  the
              graphics modes depends upon your BIOS  ROM.   This  address  is
              settable using the "/F=" option  on  the  device  specification
              line in CONFIG.SYS.

          4.  Instructions   necessary   to   prevent   the   soft    restart
              (Ctrl-Alt-Del)  from  doing the complete power  up  self  tests
              differ on different  computers.   Those necessary on the IBM-PC
              may  be  dangerous on other computers.   We  are  investigating
              possible solutions to this.

          5.  The computer may not be completely hardware equivalent with the
              IBM-PC.  If the computer's equivalence is only at  the ROM BIOS
                          FANSI-CONSOLE                                FANSI-                          _____________                                ______              level, then FANSI-CONSOLE  will  not work.  For example, FANSI-
              CONSOLE              _______              CONSOLE will definitely not work on any MS-DOS  computer with a
              terminal which is connected to the computer via a serial port.









        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               138        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               138








        FANSI-CONSOLE (tm)                      Compatibility and Limitations        _____________ ____        FANSI-CONSOLE (tm)                      Compatibility and Limitations


        This  list  of  computers  and  display  adapters  we   believe   are
                          FANSI-CONSOLE                          _____________        incompatible with FANSI-CONSOLE is not all inclusive by any means!

        Computers and display adapters we believe  are  NOT  compatible  with
        FANSI-CONSOLE        _____________        FANSI-CONSOLE:

        (Names below are all trademarks of indicated companies)

        IBM - Enhanced Graphics Adaptor -

             Most  functions  works  with   different   CRT   controller
             initialization parameters.  Use  of  /I  options allow only
             80x25 alphanumeric mode to be used.   /S  option  will  not
             work.  We expect to be able  to  eventually  fully  support
             this card, but it will take a while.

        IBM - PC jr.  -

             We haven't tested it yet.  We suspect however that the size
                FANSI-CONSOLE                _____________             of FANSI-CONSOLE and the fact that it  is  always  resident
             will  preclude  its  use   on   this   computer  with  most
             applications, because of memory  size  limitations.   There
             may also be keyboard problems.  However, we  may  create  a
             version for this computer.

        Eagle -

             Reported to work but there are extra unsupported keys.   We
             don't have enough documentation about them yet.

        IBM - Professional Graphics Adaptor -

             Not  tested  so  we  are  not  sure, but probably too  much
             different from the other adaptors.

        Tava - PC -

             Works for the  most  part,  but  on  the  machine we tried,
             Ctrl-Alt-Del  puts  the  computer   in  an  infinite  loop.
             Solution seems possible.

        Tandy 2000 -

             Same problem as Texas Instruments Professional Computer.










        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               139        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               139








        FANSI-CONSOLE (tm)                      Compatibility and Limitations        _____________ ____        FANSI-CONSOLE (tm)                      Compatibility and Limitations


        Texas Instruments - Professional Computer -

             Not a hardware  compatible  machine.  The machine does have
             enough similarities that it may be  worthwhile  for  us  to
                               FANSI-CONSOLE                               _____________             make a version of FANSI-CONSOLE  for  it.  It would turn it
             into a more compatible machine.

        Zenith Z100 -

             Same problem as Texas Instruments Professional Computer.












































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               140        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               140








        FANSI-CONSOLE (tm)                                            Credits        _____________ ____        FANSI-CONSOLE (tm)                                            Credits








                                      Chapter 9                                      Chapter 9

                                       Credits                                       Credits




        ________________________        9.1 How did you do that?


        We know you have questions about our company and how our products are
        produced.   Needless  to  say,  we  use  only  the  finest  unnatural
        ingredients.

        Hersey Micro Consulting, Inc.  is a small  new company formed in 1984
        from a  three  year old consulting business owned by Mark Hersey.  We
        are specialists in  system  software for microcomputers.  Our company
        is dedicated to promoting software portability among machines.

        FANSI-CONSOLE        _____________        FANSI-CONSOLE was conceived as a notion that there must be a  way  to
        make the IBM-PC  color  graphics  display  adaptor  to  scroll  large
        portions  of  the  screen  quickly without blinking.   Although  some
        programming was done in that direction as early as January, 1983, the
                       FANSI-CONSOLE                       _____________        programming of FANSI-CONSOLE as a product by itself  began in earnest
        in November, 1983. It was introduced to the public in October, 1984.

            FANSI-CONSOLE            _____________        The FANSI-CONSOLE source program is about 12000 lines of code written
        in Microsoft's Macro Assembler.  For some reason,  it  keeps  getting
        bigger, too.  Unlike many folks, we like  that  assembler,  including
        its primitive type checking.   In  fact,  we  wish  it  had more type
        checking.   We  use a set of macros for structured  programming  that
        give  us  nested  IF-THEN-ELSE  type   statements   and   LOOP   type
        statements.

        Some utility programs were written in C and  compiled  with  either a
        Lattice  C  compiler  (we  like the generated  code)  or  a  Computer
        Innovations C compiler (we like the library source).

        The user manual was processed by the  Mark of the Unicorn's FinalWord
        word processor.

        Programs were compiled and assembled on a Seattle  Computer  Products
        S100 bus 8086 computer running MS-DOS, which  is  sometimes  upgraded
        with a Lomas Data Products Lightning 286 board.

        Programs were tested first and most frequently on  an  IBM-PC  with a
        Tecmar Graphics Master display adaptor board and a Princeton Graphics

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               141        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               141








        FANSI-CONSOLE (tm)                                            Credits        _____________ ____        FANSI-CONSOLE (tm)                                            Credits


        color monitor.  It  also  has  an  AST  Six  Pack Plus multi-function
        board, a  Mountain  hard  disk controller, and an Interface I**2 Disk
        System.  Naturally, we use IBM-PC DOS.

        We thank these companies for  their  creative efforts and for putting
        their useful products in the marketplace.

        We also thank our beta-testers for putting up  with unstable versions
        and providing useful comments.













































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               142        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               142








        FANSI-CONSOLE (tm)                         Distribution and Licensing        _____________ ____        FANSI-CONSOLE (tm)                         Distribution and Licensing








                                      Chapter 10                                      Chapter 10

                              Distribution and Licensing                              Distribution and Licensing




                      FANSI-CONSOLE        ___________________________________________        10.1 You mean FANSI-CONSOLE isn't freeware?


                      FANSI-CONSOLE (tm)                      _____________ ____        The  program  FANSI-CONSOLE (tm) is a commercial product and  is  not
        public  domain.   It  is  not   "freeware"   either,   although   its
        distribution is similar to that of "freeware".

                  NOT                  ___        We prefer NOT to call it "freeware" for three reasons:

          1.  The name "freeware" implies something for nothing, and we still
              believe that we are  entitled  to  be paid by you for using our
              software, if you like it enough to use it.

                         abbreviated                         ___________          2.  Only  the  abbreviated  user  manual  is  on  the  distribution
              diskettes.  Several chapters describing  advanced  features  in
                                                   complete                                                   ________              detail have been removed  from  the  complete  user  manual  to
              create the abbreviated  user  manual.  The complete user manual
              is not free and must be purchased if one is desired.

          3.  "Freeware" is also a trademark of  The  Headlands  Press,  Inc.
              and not of our own.  If it were not trademarked and were merely
              a generic classification, we  would  have  less complaint about
              that aspect of things.

        Instead, perhaps we should call it "fairware".   We want things to be
        fair for you and for us.















        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               143        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               143








        FANSI-CONSOLE (tm)                         Distribution and Licensing        _____________ ____        FANSI-CONSOLE (tm)                         Distribution and Licensing


                                                     FANSI-CONSOLE                                                     _____________        The basic difference between the license for FANSI-CONSOLE  and  that
                                                       FANSI-CONSOLE                                                       _____________        of software  which  is freeware is that use of FANSI-CONSOLE beyond a
                                                     _________ _____  _______        free  trial  period,  is  subject  to  a low mandatory usage  royalty
        _______        payment  instead  of  a  voluntary usage royalty  payment  (sometimes
        called a "contribution" in the latter case).  Unlike many  commercial
        software vendors, we feel that you  are entitled to a test drive with
        our software for a free trial period.  On the other hand,  like  many
        commercial  software  vendors, we feel that if you continue  use  our
        software  you  should pay us for the privilege.  The  price  you  pay
        should still be fair, but it should not be free.












































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               144        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               144








        FANSI-CONSOLE (tm)                         Distribution and Licensing        _____________ ____        FANSI-CONSOLE (tm)                         Distribution and Licensing






                                            FANSI-CONSOLE        __________________________________________________        10.2 How are you limiting my use of FANSI-CONSOLE?


                    FANSI-CONSOLE (tm)         abbreviated                    _____________ ____         ___________        The program FANSI-CONSOLE (tm) and its abbreviated  user  manual  are
        copyrighted                                                restricted        ___________                                                __________        copyrighted  by  Hersey Micro Consulting, Inc.   We  give  restricted
        permission to make unlimited numbers of copies for  personal use.  We
                  restricted                  __________        also give restricted permission to make unlimited numbers  of  copies
        of the diskettes for distribution to others.  To  allow such copying,
              ___ ____ _________        it is not copy protected.


        10.2.1 Limitations

        The restrictions on this permission to make unlimited numbers  copies        ___ ____________ __ ____ __________ __ ____ _________ _______  ______        The restrictions on this permission to make unlimited numbers  copies
        are as follows:        ___ __ ________        are as follows:

              _______  ______  __  ___  ____ _______ _______  ___________  __          1.  Printed  copies  of  the  user manual, whether  abbreviated  or
              _________ ____ ___ __ ___________              complete, must not be distributed  without  a  written  license
              from Hersey Micro  Consulting,  Inc.   to  do so, even if it is
                                                                       FANSI-                                                                       ______              done for free and with no service charge.  All copies of FANSI-
              CONSOLE          abbreviated              _______          ___________              CONSOLE and its  abbreviated  user manual which are distributed
              to others must be on magnetic media,  such as diskettes, or via
              electronic communications such as via electronic bulletin board
              systems or electronic  information  networks.   The  recipients
              must each print  their  own  copies  of  the  abbreviated  user
              manual.

              ___ _____ __ ___  ________  ____  ______  ____  ___  ___ __ ___          2.  The parts of the  complete  user  manual  that  are  not in the
              ___________ ____ ______ ____ ___ __ ___________              abbreviated user manual must not be distributed  in  any  form,
              especially  printed  or on magnetic media,  without  a  written
              license from Hersey Micro Consulting, Inc.



















        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               145        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               145








        FANSI-CONSOLE (tm)                         Distribution and Licensing        _____________ ____        FANSI-CONSOLE (tm)                         Distribution and Licensing


              ___ ______ ___________  __  ______ ____ _______ _____ _________          3.  All copies distributed  to  others must include files identical
              __ ___ ___ ________ _____              to all the original files.  A list of files is included in this
              manual.  So the program must not  be  distributed  without  the
              abbreviated  user  manual,  for  example.   The  files  may  be
              condensed via data compression  techniques if the decompression
              process results in files identical to all the  original  files,
              and that the decompression program is included on  the media in
              object  form.   Versions  of  the program or  abbreviated  user
              manual which have been otherwise modified, or incorporated into
              other  programs  in  whole  or in part,  must  not  be  further
              distributed.  Files indicating program  patches, or user manual
              addenda, may be added to the media as separate files, providing
              that there  is  room for such files on the media.  Such changes
              must not  remove  or  change the copyright notices found in the
              program or abbreviated user manual.

                       FANSI-CONSOLE              ___  __  _____________  ______  ___  ____  __ _____ ___ __  ___          4.  Use  of  FANSI-CONSOLE  beyond  ten  days  of first use of  the
              ________ ___ _____ _____ ________ __  _______  __  _  _________              program, the "free trial period", is  subject  to  a  mandatory
              _____  _______  _______  __  ___  _______              usage  royalty  payment  of  $25  (MI+4%)  (United States)  per
              computer console (CRT) on which it may be used  simultaneously.
              This is true unless you have received  the  published  (printed
              and bound) form of the complete user  manual, the cost of which
              includes the usage royalty payment  for  one  computer  console
              (CRT).  This usage royalty must be delivered directly to Hersey
              Micro  Consulting,  Inc.  at the address on the cover  page  of
              this manual.  The free trial period is intended to allow you to
              try the program before paying for it.  If at  the  end  of  the
              free trial period, you decide you  do not want to pay the usage
              royalty, this may be done  providing  all copies of the program
              which are or will be in your possession are never used  by  you
              again.  Even in this case  they  may  be  further  distributed.
              Obviously, even though payment is  legally  mandatory,  we  are
              relying on your honesty, because in most  cases, we do not have
              much capability to enforce it.  Remember that your payment will
              help us  to  afford to develop other fine programs that you may
              also be interested in using.

                                      FANSI-CONSOLE                                      _____________          5.  Serial reuse, or moving FANSI-CONSOLE from one computer console
              to use it on another, is specifically allowed.  We require that
                      FANSI-CONSOLE                      _____________              either  FANSI-CONSOLE  is  first   removed  from  the  original
              computer console  (CRT)  before  use on the second, or that the
              original computer console (CRT) be unattended during use on the
                            FANSI-CONSOLE                            _____________              second.  Thus FANSI-CONSOLE  is  only  in  active  use  on  one
              computer console at a time.  This is roughly  equivalent to the
              concept of a per user license.









        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               146        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               146








        FANSI-CONSOLE (tm)                         Distribution and Licensing        _____________ ____        FANSI-CONSOLE (tm)                         Distribution and Licensing


                             FANSI-CONSOLE              __________  __ _____________ ______ ___________ __ ______  ____          6.  Recipients  of FANSI-CONSOLE copies distributed to others  must
              ___   __   _______  ___  ___  _____   _______   __   __________              not   be   charged  for  the  usage   royalty   by   unlicensed
              ____________              distributors.  In fact, the  recipients  must  be encouraged to
              follow  the  terms  of this  licensing  agreement.   Recipients
              should note that this means that payment of  such  distribution
              fees does not cover the usage royalty, which must still be paid
              to Hersey Micro Consulting, Inc., if the program is used beyond
              the free trial period.  Distribution charges (such as materials
              and postage) may be made  if they are no more than $10 per copy
              and  no  more  than  that  charged  for other media of  similar
              construction,   capacity,   and   quantity   from   the    same
              distributor.










































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               147        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               147








        FANSI-CONSOLE (tm)                         Distribution and Licensing        _____________ ____        FANSI-CONSOLE (tm)                         Distribution and Licensing




        10.2.2 Rights

        Payment of the usage royalty fee entitles you to:

          1.  A  copy  of the next program update (does not  include  printed
              complete user manual) directly from  us.   If  you  describe  a
              feature you would like included, and we feel that we are likely
              to add some similar feature, we will delay  shipment until that
              similar feature is supported.

                           use                     FANSI-CONSOLE                           ___                     _____________          2.  A license to use updated versions of FANSI-CONSOLE,  if you can
                                                                          not                                                                          ___              obtain them, for no additional usage royalty fee.   It does not
              include the costs of distributing such updated versions.

                                        FANSI-CONSOLE                                        _____________          3.  Request help with solving FANSI-CONSOLE related problems.  Note
              however, that we do not  guarantee  that telephone help will be
              provided to each licensed user.  Remember that such things cost
              a good deal of money  to support.  We hope to set up a bulletin
              board system to provide information about new  versions  and  a
              mechanism for initiating problem resolution.

          4.  Assignment of a new serial number.  It will  be  placed  in the
              version heading of any update you receive directly from us.  It
              should be used as an identifying number when requesting updates
              or help.



























        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               148        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               148








        FANSI-CONSOLE (tm)                         Distribution and Licensing        _____________ ____        FANSI-CONSOLE (tm)                         Distribution and Licensing






                              FANSI-CONSOLE        ____________________________________________________        10.3 How do I know if FANSI-CONSOLE is right for me?





        10.3.1 DISCLAIMER        10.3.1 DISCLAIMER

        FANSI-CONSOLE        _____________        FANSI-CONSOLE and its user manual are provided "as is".  If you don't
        like it after the free  trial period, don't use it.  If you don't use
        it after the free trial period,  don't pay for it.  We cannot warrant
        it for all possible purposes, as we know it has limitations.  We have
        even tried to notify you of the limitations  we  already  know about.
        We  cannot  warrant it for your specific purposes, because  it  would
        cost us much more to determine its suitability for your purposes than
        we are charging.

                                                                FANSI-CONSOLE                                                                _____________        It is  up  to you to determine the suitability of using FANSI-CONSOLE
        with any other program or with any computer.   Mention  of  any other
        program or a computer in this manual is not  a  guarantee  by  Hersey
                                                           FANSI-CONSOLE                                                           _____________        Micro Consulting, Inc.  of  suitability  of  using FANSI-CONSOLE with
        that other program or computer.  We do occasionally  make mistakes in
        the user manuals, and they cannot always be rectified by changing the
        program.

        In no event will Hersey Micro Consulting,  Inc.  be liable, either to
        you  or to any other  party,  for  any  damages,  including  loss  of
        profits, lost savings,  or  other incidental or consequential damages
                                                       FANSI-CONSOLE                                                       _____________        arising out of the use of  or inability to use FANSI-CONSOLE, even if
        we have been advised of the possibility of such damages.

        Since you may have received this  version  from  someone  other  than
        Hersey Micro Consulting, Inc., it may have been mangled on its way to
        you.  We obviously can't  warrant  that  no  one  has  done that.  We
        certainly hope no one will do that, anyway.

        We reserve the right to make modifications to  the  program  and user
        manuals without notification to you.












        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               149        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               149








        FANSI-CONSOLE (tm)                         Distribution and Licensing        _____________ ____        FANSI-CONSOLE (tm)                         Distribution and Licensing






                                              FANSI-CONSOLE        ____________________________________________________        10.4 How do I get updated versions of FANSI-CONSOLE?


        All prices below are subject  to change if our costs get out of hand.
        We  will  try  to  hold  the  price as low as possible, to  encourage
        everyone           FANSI-CONSOLE        ________           _____________        everyone  to  use  FANSI-CONSOLE.    We've   already   been  told  by
        distributors  that  our price is ridiculously low, but we  will  keep
        these prices  as  long  as  we  can.  It is also the case that as the
        program goes in function, the printed user  manual will grow in size,
        and this will require a higher price for the manual.

        Updated versions of the  program  and  abbreviated  user  manual,  or
        versions on differently formatted  diskettes,  may  be purchased from
        Hersey Micro Consulting, Inc.  for $10 (MI+4%)  per  diskette.   This
        requires a previously or simultaneously paid license fee.  The  price
        includes the media, so please don't send us any.  We don't  want  our
        mailperson to be overwhelmed with incoming packages.  Of course,  you
        can also get updates from other customers of Hersey Micro Consulting,
        Inc., for whatever they charge.

        Diskettes are currently available in 8-inch  SSSD  formats  and  most
        5-inch DSDD formats.  We also expect availability in some  sub-4-inch
        formats when  such  formats  become more common.  We're sorry, but we
        cannot directly support  formats  requiring  one-of-a-kind  hardware,
        such as Victor 9000 (Sirius  1),  Apple  II,  or  any  type  of  hard
        sectored diskettes.  Orders  requiring  such  one-of-a-kind  hardware
        will require  an  extra  $25 processing charge per order, assuming we
        can find such hardware to borrow.

        We provide software  update  notice  service  for a $25 one time fee.
        This requires a previously or simultaneously paid license fee.   This
        puts you on our mailing list of customers who are interested in being
        directly notified of the availability of  newer  versions.   We  will
        send you a notice giving an overview of new features and bug fixes in
        new versions on a quarterly basis.  Then you  can  decide  whether to
        obtain a new version, either directly from  us or elsewhere.  We will
        also notify you of the availability of other programs from us.













        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               150        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               150








        FANSI-CONSOLE (tm)                         Distribution and Licensing        _____________ ____        FANSI-CONSOLE (tm)                         Distribution and Licensing






        ______________________________________________________        10.5 What do we pay if we have more than one computer?


        Site licenses may be purchased from  Hersey  Micro  Consulting,  Inc.
        The charge for such a site license is $25 (MI+4%) (United States) per
                                                                       FANSI-                                                                       ______        computer console (CRT) owned by the licensing entity  on which FANSI-
        CONSOLE        _______        CONSOLE may be used simultaneously  (fair  estimates  accepted).   If
        additional  computers  are  purchased  by the licensing  entity,  the
        royalty should be recalculated and the increase paid annually.   Site
        licenses cover  all  use  by all employees or students, regardless of
        whether  the  computers used are owned by the licensing  entity.   So
        home  use  is included, for example.  Site license pricing  does  not
        include any printed  user  manuals.   They  may  be  purchased for an
        additional $25 (MI+4%) each.  Quantity discounts are available.




































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               151        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               151








        FANSI-CONSOLE (tm)                         Distribution and Licensing        _____________ ____        FANSI-CONSOLE (tm)                         Distribution and Licensing






                                          FANSI-CONSOLE        ____________________________________________________________        10.6 Can I get a printed complete FANSI-CONSOLE user manual?


        Printed user manuals in "IBM  standard"  size loose leaf binders with
        slip  covers  may be  purchased  for  $50  (MI+4%).   The  $50  price
        includes: the  printed  manual;  a usage royalty fee for one computer
        console (CRT); one distribution  diskette  with  the  program  and  a
        magnetically copyable version  of  the abbreviated user manual.  This
        is  the  "commercial"  version  of  the  program.  When the order  is
        prepaid, the  price  also  includes ground shipping by UPS within the
        USA.  Other shipping arrangements require a shipping charge.

                        FANSI-CONSOLE                        _____________        If you received FANSI-CONSOLE from  us  or  from  another  commercial
        product vendor,  and  did not receive a printed user manual, then you
                                                                FANSI-CONSOLE                                                                _____________        may have received our registration  coupon  with  your  FANSI-CONSOLE
        serial  number  on it.  Receiving that coupon means that  vendor  has
                              FANSI-CONSOLE                              _____________        paid us to distribute FANSI-CONSOLE with their product,  and it means
        that your  usage  royalty  for one computer console (CRT) has already
        been  paid  for  you  by  the  vendor.  If you did  not  receive  our
        registration coupon with your serial number on  it, or a printed user
        manual, then the vendor did not pay your usage royalty fee,  and  you
        must pay  it  yourself.   The registration coupon is redeemable for a
        printed user manual at the reduced cost of $25 (MI+4%).

        Updates for the complete user manual will cost  $25 (MI+4%), assuming
        you've purchased the commercial  version  of  the  program,  or  have
        otherwise payed the usage royalty licence fee.

        We didn't include  the  complete  user  manual  on  the  distribution
        diskettes for several reasons:

              ________ __  ________  ___  __ _ _________ _____          1.  Frankly, it  wouldn't  fit  in a printable form.  At least, not
              the way we want it printed.

          2.  Using data compression might have  made  it fit, but would have
              scared  away   some   potential   users,   and   made  printing
              inconvenient.

          3.  An abbreviated user manual is quicker and less discouraging  to
              print, or to download from a bulletin board system.

          4.  We wanted some control over how it got  abbreviated, for people
              desiring only a shorter form.

          5.  The  part  we  left  out   was   mostly  of  interest  only  to
              programmers.




        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               152        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               152








        FANSI-CONSOLE (tm)                         Distribution and Licensing        _____________ ____        FANSI-CONSOLE (tm)                         Distribution and Licensing


          6.  It  provides  some small encouragement to pay us for  our  hard
              work.




















































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               153        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               153








        FANSI-CONSOLE (tm)                         Distribution and Licensing        _____________ ____        FANSI-CONSOLE (tm)                         Distribution and Licensing






                               FANSI-CONSOLE        __________________________________________________________        10.7 Can I publish the FANSI-CONSOLE complete user manual?


                                FANSI-CONSOLE                                _____________        You may want to include FANSI-CONSOLE with your  hardware or software
        product.  Companies interested in publishing the complete user manual
        should contact  us.   We would prefer to program than to publish!  We
        can provide you with a license to publish  the  complete  user manual
        with  a  distribution diskette; or we can provide you  a  license  to
        distribute  diskettes  with   a   serialized   registration   coupons
        redeemable for reduced cost printed user manuals.  The  license  cost
        includes  the  usage royalty fee for one computer console  (CRT)  for
        each recipient of a published complete user manual, or the serialized
        registration coupon.  Essentially, all we are doing is  selling you a
        particular lot of serial numbers and a  clear  conscience.   However,
        your customer gets an even bigger bargain on our product.

        Generally, we would prefer that you use one or the other of the above
        licenses  if  you  distribute   our   software   with  your  product.
        Distributing  our  software  with  your product without  the  license
        falsely implies to  the  customer  that  you've paid us a royalty and
        therefore that customer has already paid to use our software.




                           FANSI-CONSOLE        ________________________________________________        10.8 Can I buy the FANSI-CONSOLE program source?


                                                                       FANSI-                                                                       ______        We would  be  happy  to  provide  you with the source code for FANSI-
        CONSOLE        _______        CONSOLE, if  you  are  willing  to  sign  a  non-exclusive  licensing
        agreement, and pay $250,000 U.S.  dollars  for the privilege.  For an
        even larger sum, we might even allow you to publish the  source.   We
        obviously don't expect too many takers.  Although we  don't expect to
        become millionaires  selling  this  program, we do have some stake in
        keeping the source to ourselves until we have  made  some  money from
        our efforts.














        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               154        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.               154








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)



                           FANSI-CONSOLE                           _____________                           FANSI-CONSOLE REGISTRATION FORM

        Person completing form:

        Date:

        Company:

        Address:



        When did you first receive this product:



        Release number:

        Old serial number:

        What kind of computer are you using it on:

        Comments:






























        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)
























































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)



        Hersey Micro Consulting, Inc.           Invoice # 8401
        P.O. Box 8276                           Michigan and Federal
        Ann Arbor, Michigan USA  48107          EIN 38-2532624
        (313) 994-3259                          Date:    /    /


        Product                 Quantity Price Each Item Total

        FANSI-CONSOLE        _____________        FANSI-CONSOLE:

        complete user manual        ___ @ $50.00 = ______

        (includes royalty & disk)

        software usage royalty      ___ @ $25.00 = ______

        (includes next update disk)

        software update disk DSDD   ___ @ $10.00 = ______

        (requires paid usage royalty)

        user manual update          ___ @ $25.00 = ______

        (requires paid usage royalty)

        update notice service       ___ @ $25.00 = ______

        (requires paid usage royalty)


        Subtotal:                                  ______


        4% sales tax (Michigan residents) x0.04=   ______
        Shipping if not UPS ground                 ______


        Total:                                     ______

        Make checks payable to: Hersey Micro Consulting, Inc.
        MasterCharge and Visa are accepted.

        Card number: ____________________ Expires: ______

        You should retain this a copy of this invoice for your tax records.







        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)



                 FANSI-CONSOLE                 _____________                 FANSI-CONSOLE USAGE AND PROBLEM REPORT QUESTIONNAIRE

        We at Hersey Micro Consulting greatly appreciate your taking the time
        to complete this questionnaire.   Your  suggestions  and comments are
        important to us, as they help us both to  evaluate  and  improve  our
        products.  Please feel  free  to  file  this report with us more than
        once.

        Person completing form:

        Date:

        Company:

        Address:



        When did you first receive this product:

        Release number:

        Serial number:

        What kind of computer was it used on:



        During the usage period, about how many hours per  day  did  you  use
        this product on average?


        Do you have  any  experience  with  similar  products,  even on other
        computers?  If so, please describe the products and computers.






        How long have been using computers?



        Please give a brief description of your business and how this product
        was used:







        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


        Using a scale of 1 to 10 (1=terrible, 5=average, 10=excellent) please
        indicate your general satisfaction with the following:

        The product on the whole:

        The user manual:

        The setup procedures:

        The ease of using this product:

        The practicality or usefulness of this product:

        The performance of this product:

        The help provided by Hersey Micro Consulting:

        The following questions  may  require more lengthy responses.  Please
        use the reverse side of this sheet or additional sheets of  paper  as
        necessary.

        What would you say are the BEST features of this product?






        What would you say are the WORST features of this product?






        List any extraneous or useless features of this product that you have
        noticed.






        List any enhancements  you  would  like  to see added to the existing
        features of this product.









        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


        Describe any problems you have encountered  in  using  this  product,
        including examples if possible.




















































        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)






                                        Index


        /A option, attributes  28
        /B option, blinking scroll  29
        /C option, color what you can  29, 67, 111
        /F option, font table address  30, 138
        /G option, Ctrl-G bell length  30
        /H option, horizontal retrace delay  30
        /I option, controller initialization parameters  31
        /K option, key bell frequency  31
        /L option  22
        /L option, lock on Scroll-Lock  21, 31, 68
        /M option, memory allocated  32
        /N option, no color display  32, 68, 111
        /O option, one finger typing  33
        /S option, screen save timeout  33
        /T option  43, 45, 53
        /T option, use ANSI X3.64 TTY ROM BIOS  34
        /V option, vertical retrace delay  35
        /W option, word wide screen write  35
        /X option, extensions  35
        /Y option  15, 110, 125
        /Y option, you should be so compatible  36, 67
        50 lines  7
        FCONSOLE.DEV  13, 14, 16, 24
        abbreviated user manual  11, 12
        access methods, screen  38
        Alt-Ctrl-Caps  127
        Alt-Ctrl-Down  37, 67, 125
        Alt-Ctrl-Esc  128
        Alt-Ctrl-Ins  6, 121
        Alt-Ctrl-Num-Lock  69, 122
        Alt-Ctrl-Scroll-Lock  126
        Alt-Ctrl-Tab  128
        Alt-Ctrl-Up  37, 67, 125
        ANSI mode  54
        ANSI X3.64  3, 34
        ANSI X3.64 escape sequences  41, 42, 44, 51
        ANSI X3.64 name table  97
        ANSI.SYS  42
        ANSI.SYS device driver  2, 3, 14, 24, 26, 42, 49, 67, 101
        ANSI40.TXT  43
        ANSI80.TXT  43
        assembly language, escape sequences  48
        assignment strings  118
        attribute  29
        attributes  28, 32
        auto repeat keyboard keys  83

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


        auto wrap mode  96
        back space  54
        background color  29, 32
        background colors  86
        backward  54, 57, 58
        BASIC, escape sequences  45
        BBS  152
        beginning state  82
        BEL  54
        bell  54
        bell frequency  31
        bell length  30
        BIOS  110
        BIOS calls  102
        BIOS calls, screen  110
        BIOS, keyboard  104
        BIOS, TTY calls ANSI X3.64  34
        blinking  86
        blinking, getting rid of the scroll  29
        bold  86
        breakpoint  6, 121
        BS  54
        BSLASH  51
        BUFFERS=20  17
        bugs  130
        bulletin board system  152
        C language, escape sequences  46
        CARET  51
        carriage return  57
        CBT  54
        CHA  55
        character delete  60
        character erase  64
        character insert  75
        character names  51
        cheating  102
        CHT  55
        CK  55
        CNL  56
        color  29, 32, 67, 68
        color ROM BIOS calls  32
        color what you can  29
        colors  86
        commercial version  152
        compatibility  36, 67
        compatible computers  135
        compatible programs  132
        complete user manual  152
        compression  152
        computer independence  38
        CONFIG.SYS  14, 15, 16, 17, 24, 26, 27
        console  1
        console driver  14

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


        control sequence introducer  57
        controller initialization  31
        conventions  51
        CPL  56
        CPR  56
        CR  57
        CSI  57
        CTC  57
        Ctrl-6  22
        Ctrl-Break  22, 63, 76
        Ctrl-C  22, 63, 76
        Ctrl-Equals  22
        Ctrl-F  21
        Ctrl-G  30, 54
        Ctrl-H  54
        Ctrl-I  70
        Ctrl-J  77
        Ctrl-K  96
        Ctrl-M  57
        Ctrl-Num-Lock  21, 22, 31
        Ctrl-S  21, 22, 31
        Ctrl-[  66
        CTTY  39
        CUB  58
        CUD  58
        CUF  58
        CUP  59
        current graphics rendition  29, 83, 85
        cursor backward  58
        cursor backward tab  54
        cursor down  58, 59
        cursor forward  58
        cursor horizontal absolute  55
        cursor horizontal tab  55
        cursor key mode  55
        cursor left  58
        cursor movement  54, 55, 56, 57, 58, 59, 70, 71, 76, 77, 78, 79, 81,
        82, 83, 93, 95, 96
        cursor next line  56
        cursor position  59
        cursor position report  56
        cursor preceding line  56
        cursor right  58
        cursor tabulation control  57
        cursor up  59
        cursor vertical absolute  95
        cursor vertical tabulation  59
        CUU  59
        CVT  59
        DA  28, 60
        data compression  152
        DCH  60
        DEC VT100 emulation  4, 69, 122

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


        DEC VT52 emulation  4
        DEC-ANM  54
        DEC-ARM  83
        DEC-AWM  96
        DEC-CKM  55
        DEC-KPAM  77
        DEC-KPNM  77
        DEC-OM  79
        DEC-RM  60
        DEC-SCNM  83
        delay, horizontal retrace  30
        delay, vertical retrace  35
        delete character  60
        delete line  63
        device attribute  60
        device driver  14, 15, 25
        device status report  64
        DEVICE=  14
        disable keyboard  63, 76
        disable manual input  63
        disclaimer  149
        display erase  65
        display, BIOS calls  110
        display, software interrupt  110
        distribution  143
        distribution diskette  11
        DL  63
        DLE  63
        DMI  63
        documentation  11, 12, 152
        down  56, 58, 59, 76, 77
        DSR  64
        DVORAK.TXT  43
        ECH  64
        ED  65
        editing mode, horizontal  69
        editing mode, vertical  95
        EL  65
        EMI  66
        emulation, DEC VT100  4, 69, 122
        emulation, DEC VT52/Heath H19/Zenith Z100  4
        enable keyboard  66, 76
        enable manual input  66
        erase character  64
        erase display  65
        erase line  65
        erase screen  65
        ESC  51, 66
        escape  66
        escape sequence name table  97
        escape sequences  3
        extensions  35
        extra distribution files  129

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


        FANSI  1
        FANSI-CMP  67, 110
        FANSI-COLOR  67, 111
        FANSI-IBM  67
        FANSI-LOCK  68
        FANSI-NOCOLOR  68, 111
        FANSI-RM  37, 66
        FANSI-SM  37, 68
        FANSI-VT100  69
        fast  35, 36
        FCONSOLE.DEV  27
        file list  11
        files, extra distribution  129
        fixed disk  13
        flashing, getting rid of the scroll  29
        flicker, getting rid of the scroll  29
        font  30
        foreground color  29, 32
        foreground colors  86
        forward  58
        free trial period  146
        freeware  143
        graphics font  30
        graphics rendition  29, 32, 83, 85
        GRAVE  51
        hard disk  13
        hardware requirements  2
        hashing  30
        Heath H19 emulation  4
        HEM  69
        home position  81
        horizontal and vertical position  71
        horizontal editing mode  69
        horizontal position absolute  70
        horizontal position relative  70
        horizontal retrace delay  30
        horizontal tab  70
        horizontal tabulation set  71
        HPA  70
        HPR  70
        HT  70
        HTS  71
        HVP  71
        IBM-KKR  72, 118, 126
        IBM-RM  72, 74, 88
        IBM-SM  73, 74, 88
        ICH  75
        ID  75
        identify  75
        IL  75
        incompatible computers  138
        incompatible programs  136
        IND  76

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


        index  10, 76
        initial state  82
        initializing crt controller  31
        insert character  75
        insert line  75
        insert mode  76
        installing FCONSOLE, simple  11
        installing FANSI-CONSOLE, detailed  27
        interlaced mode  7
        internal parameters  31
        interrupt vector, reservation violation  39
        interrupt, keyboard  104
        interrupt, screen  110
        inverse video  86
        IRM  76
        joke  10, 16, 141
        KAM  76
        key pad alternate mode  77
        key pad numeric mode  77
        key reassignment  72
        keyboard action mode  76
        keyboard disable  63, 76
        keyboard enable  66, 76
        keyboard replacement strings  118
        keyboard, BIOS calls  104
        keyboard, software interrupt  104
        KKR  72
        KKR   118, 126
        KPAM  77
        KPNM  77
        left  54, 57, 58
        LF  77
        limitations  130
        line delete  63
        line erase  65
        line feed  77
        line feed new line mode  78
        line insert  75
        literal next character  63
        LNM  78
        loadable device driver  25
        locking scroll  31
        manual  11, 12, 152
        memory limit  32
        names, table of ANSI X3.64 escape sequence  97
        NEL  78
        next line  78
        next page  78
        NP  78
        one finger pause  31
        one finger typing  33
        option  26
        options, installation  27

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


        ORIG  79
        origin mode  79
        output redirection  39
        P1  51
        P2  51
        P3  51
        P4  51
        painting  2
        parameter  26
        parameters  51
        parameters, installation  27
        parameters, internal  31
        PASCAL, escape sequences  47
        pause  6, 21, 22, 31
        Pi  51
        positioning unit mode  80
        PP  79
        prefix  57
        previous page  79
        primary graphics rendition  29, 32, 83, 85
        print spoolers  20
        printed user manuals  152
        problem, Alt-Ctrl-Ins causing breakpoint in wrong place  121
        problem, bad or missing FCONSOLE.DEV  24
        problem, bad or missing FCONSOLE.DEVLE.DEV  14
        problem, blank screen  15
        problem, blinking  29
        problem, character is not displayed  63
        problem, characters overwritten  36
        problem, characters written in wrong place  36
        problem, confuses keyboard replacement program  124
        problem, ctrl-6 key doesn't work  22
        problem, Ctrl-P key  18
        problem, Ctrl-PrtSc key  18
        problem, Ctrl-X key  18
        problem, different colors after restore  34
        problem, disk access increases  20
        problem, escape key  18
        problem, everything is in black and white  74, 88
        problem, flashing  29
        problem, flicker  29
        problem, hashing  30
        problem, installation  16
        problem, memory usage  15, 138
        problem, not enough memory  20
        problem, not replacing keyboard keys  72
        problem, prompt doesn't set colors with echo off  18
        problem, screen distorted after restore  34
        problem, screen save does not work  34
        problem, scroll-lock key  31
        problem, slow scroll  29
        problem, snow  30
        problem, strange shape characters  30

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


        problem, tab stops don't get set right  70
        problem, unreadable characters  32
        problem, won't change colors  18
        problem, wrong attributes  29
        problem, wrong colors  29
        problem, wrong colors after program ends  18
        problems how to check that FCONSOLE is cause  20
        problems, Zenith display does not turn off  35
        program source  154
        programming escape sequences  44
        PROMPT  18
        Ps  51
        PUM  80
        ram disk  15
        RAM disks  20
        ramdisk  26
        raw mode  70
        RC  80
        RCC  80
        RCP  81
        redirection  39
        removing FCONSOLE  24
        REP  81
        repeat character  81
        repeat keyboard keys  83
        replacement mode  76
        replacement strings  118
        report  56, 60, 64, 80
        report cursor content  80
        reset modes  60, 66, 72, 82
        reset to initial state  82
        restore cursor position  81
        retrace delay, horizontal  30
        retrace delay, vertical  35
        return  57
        reverse index  81
        reverse video  86
        RI  81
        right  58
        RIS  82
        RM  60, 66, 72, 82
        ROM BIOS  7, 14, 110
        ROM BIOS calls  102
        ROM BIOS, keyboard  104
        royalty  144
        RPT  83
        save cursor position  83
        SC  83
        SCP  83
        screen access methods  38
        screen display mode  29, 30, 32, 34, 35, 36, 72, 73, 74, 85, 88
        screen display redirection  39
        screen erase  65

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


        screen mode  83
        screen painting  2
        screen save timeout  5, 33
        screen, BIOS calls  110
        screen, software interrupt  110
        SCRN  83
        scroll down  84
        scroll left  89
        scroll lock  68
        scroll right  92
        scroll slow  29
        scroll up  94
        Scroll-Lock  6, 21, 22, 31
        scrolling  63, 75, 76, 77, 78, 79, 81, 84, 89, 92, 93, 94
        scrolling region  93
        scrolling regions  4, 93
        SD  84
        set graphics rendition  85
        set modes  62, 68, 73, 90
        set scrolling region  93
        setting up FCONSOLE, simple  11
        SGR  73, 85
        shift keys  33
        Shift-PrtSc  23
        site licenses  151
        SL  89
        slow  35, 36
        slow scroll  29
        SM  62, 73, 90
        snow  30
        software interrupt, keyboard  104
        software interrupt, screen  110
        source program  154
        SP  51
        speed  35, 36
        SPIT.EXE  43
        SR  92
        SSR  93
        starting state  82
        status report  64
        SU  94
        switches, installation  27
        system disk  14, 17
        tab  55, 70, 96
        tab stop, clear  57
        tab stop, set  57
        tabulation clear  94
        TBC  94
        terminal emulation  4
        text movement  60, 63, 75, 76, 77, 78, 79, 81, 84, 89, 92, 93, 94, 95
        TILDE  51
        timeout, screen save  5, 33
        trial period  146

        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.








        FANSI-CONSOLE (tm)        _____________ ____        FANSI-CONSOLE (tm)


        TTY, BIOS calls ANSI X3.64  34, 116
        typeahead buffer  5, 14, 136
        typeahead flushing  5
        typeahead limit  5
        typeahead, flushing  21
        underlining  86
        uninstalling FCONSOLE  24
        unit mode  80
        up  56, 59
        update notice service  150
        updated versions  150
        user manual  11, 12, 152
        using FCONSOLE, simple  21
        VEM  95
        verify distribution diskette  11
        versions  131
        vertical editing mode  95
        vertical position absolute  95
        vertical position relative  95
        vertical retrace delay  35
        vertical tab  96
        vertical tabulation set  96
        VPA  95
        VPR  95
        VT  96
        VT100 emulation  4, 69, 122
        VT52 emulation  4
        VT52 mode  54
        VTS  96
        windows  4, 8, 93
        word wide screen move  35
        WRAP  96
        wrapping mode, auto  96
        writing escape sequences  44
        Z100 emulation  4



















        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.        (C) Copyright 1984-85 Hersey Micro Consulting, Inc.